## Slide 1
MK6 vs XX-II/IIS (Internal Confidential)

## Slide 2: Measured Performance
Specifications vs Actual Measured
INTERNAL ONLY

## Slide 3: Summary Scoring
Model | General | Electricals | Hydraulics | Mechanics | Total Score
JM168-MK6 |  |  |  |  | 16
XX1600II |  |  |  |  | 12
XX1600IIS |  |  |  |  | 12

## Slide 4: Highest Actual Measured Speed for All Specifications at 99% Settings
 |  | Units | XX1600II | XX1600IIS | JM168-MK6
Max. Clamp Closing Speed |  | mm/s | 696 | 638 | 817 (+28%)
Max. Clamp Opening Speed |  | mm/s | 1,197 | 1,010 | 1,313 (+30%)
Max. Injection Speed |  | mm/s | 104 | 100 | 108 (+8%)
Max. Plasticizing Speed |  | rpm | 206 | 217 | 224 (+9%)
Ejector | Max. Eject Speed | mm/s | 375 | 295 | 527 (+79%)
 | Max. Return Speed | mm/s | 355 | 341 | 496 (+45%)
Carri-age | Max. Fwd Speed | mm/s | 50 |  | 102 (2x)
 | Max. Bwd Speed | mm/s | 62 |  | 77 (+24%)
Max. Mould Adj. Speed |  | mm/s | 2.0 | 2.3 | 2.5 (+25%)

## Slide 5: Comparison in Actual Production
 | XX1600II | JM168-MK6
Part | Thin-Walled Enclosure Part | 
Resin | ABS | 
Screw Diameter | D45 | D46
Shot Weight | 28.1g | 28.1g
Cycle Time | 29.1 sec. | 21.2 sec. (-27%)
Productivity | 120 / hour | 169 / hour (+41%)
Electricity Consumption | 796 kW/kg | 634 kW/kg (-19%)

## Slide 6: What Makes The Difference
Precision Hydraulics®
for the MK6

## Slide 7: Precision Hydraulics®
Next-Gen computer control algorithms and hydraulics circuit design
Developed by senior Japanese engineers with decades of technical expertise, using advanced hydraulics simulation software
Enhancement of 3rd Gen Servo-Pump technology: from 3G to 4G
Eliminates unnecessary pressure drops for ultimate precision
Precision at HIGH SPEED
(JM168-MK6 has sustainable dry cycle of only 1.9s)
Rock-Solid Stability
(little vibrations and shocks even running at max. speed)
High Repeatability
(tolerances < 0.05%)

## Slide 8: Injection Performance
Comparisons of Injection Specs &
Actual Measurements
INTERNAL ONLY

## Slide 9: Injection Speed Response (0 → 99%)
Injection speed response curves from 0-99%
Smaller numbers are better
Look for: smoothness, no fluctuations, no overshoots
XX1600II
XX1600IIS
JM168-MK6
220ms
320ms
300ms
Command
Actual Speed
Position

## Slide 10: The Importance of Speedy Response
Time
Speed
JM168-MK6
XX1600II
XX1600IIS
220ms
300ms
320ms
Notes
Response is similar to a sports car – 0-100kph acceleration time
Smooth rides at high speed demands quick responses
Snappy responses reduce cycle times, increase productivity
Quick responses are particularly beneficial to difficult or thin-walled moulding processes
(0 → 99%)

## Slide 11: Injection Pressure Control
Look for: smoothness, no fluctuations, no overshoots
Injection pressure control is vital to ultimate part quality
Special materials (e.g. engineering resins) are particularly sensitive to pressure fluctuations
Stable injection pressure has a definitive impact on yield rates
MK6 has superior pressure control
XX1600II
XX1600IIS
JM168-MK6

## Slide 12: Injection Base Pressure and Pressure Drop
10
XX1600IIS
XX1600II
15
15
JM168-MK6
8
4
Lose
21%
Lose
35%
Smaller numbers are better
Base pressure and pressure drops are non-work wasted energy dispersed as heat, requiring even more energy to cool
High base pressure or pressure drops leads to significantly lower power efficiency and energy saving
MK6’s Precision Hydraulics® all but eliminates pressure drops and has very low base pressure
Pressure Drop (bar)
Base
Pressure
(bar)
Base
Pressure
(bar)

## Slide 13: Injection Pressure: Spec. vs Actual Measured
188
XX1600IIS
XX1600II
147
155
JM168-MK6
22
23
diff
15%
diff
15%
Injection pressure: bigger numbers are better
Higher injection pressure means better and more consistent part quality
Should not exist material differences between actual measured pressure vs specification
Mismatch between spec. and actual
(MPa)
Actual
Measured
(MPa)
Spec.: 169
Spec.: 178
Spec.: 188
Actual: 192

## Slide 14: Nozzle Protection Guard
XX1600II
XX1600IIS
JM168-MK6
Easy to operate
not convenient
Easy to operate
Window
Window
no window

## Slide 15: Injection Carriage Cylinders
XX1600II
XX1600IIS
JM168-MK6
Completely balanced
for high speed
Forces unbalanced
Hinders high-speed
injection
Forces unbalanced
Hinders high-speed
injection
Dual Balanced
Single Cylinder
Single Cylinder

## Slide 16: Injection Base
XX1600II
XX1600IIS
JM168-MK6
Smoothness for
high-speed injection
Smoothness for
high-speed injection
not designed for
high-speed injection
Linear Rails
traditional guide rods
Linear Rails

## Slide 17: Holding Performance
Comparisons of Holding Specs &
Actual Measurements
INTERNAL ONLY

## Slide 18: Holding Pressure Response (0 → 99%)
Holding pressure response curves from 0-99%
Smaller numbers are better
Look for: smoothness, no fluctuations, no overshoots
Stable holding pressure is vital to part quality and high yield
XX-IIS degrades response speed to avoid overshoots from higher system pressure
XX1600II
XX1600IIS
JM168-MK6
270ms
590ms
290ms
Cmd.
Pres.

## Slide 19: Pressure Control
Look for: smoothness, no fluctuations, no overshoots
XX-II/IIS have lower quality pressure control – i.e. high fluctuations and overshoots
MK6’s innovative Precision Hydraulics® technology yields precise pressure control
Precise pressure control is vital for demanding, pressure-sensitive applications such as optical parts
XX1600II
XX1600IIS
JM168-MK6

## Slide 20: V/P Switch-Over Response
Look for: smoothness, no fluctuations, no overshoots
Precise and stable V/P switch-over is vital for demanding applications requiring precise dosing
XX1600II
XX1600IIS
JM168-MK6
Injection Command
Actual Pressure
Pressure Command
Patented
Technology

## Slide 21: Plasticizing Performance
Comparisions of Specs &
Actual Measurements
INTERNAL ONLY

## Slide 22: Plasticizing Motor Size and Torque
XX1600II
XX1600IIS
JM168-MK6
Size: 500cc
Unit torque: 80 Nm
Size: 400cc
Unit torque: 51 Nm
Size: 500cc
Unit torque: 66 Nm
Fast and Strong
slow and weak
even slower and weaker!

## Slide 23: Plasticizing Torque
Model | Screw Diam. | Flow Rate | Unit Torque | Max. Pressure | Max. Torque
JM168-MK6 | 46mm | 500cc | 8 | 175 bar | 1,400
XX1600II | 45mm | 500cc | 6.6 | 140 bar | 924
XX1600IIS | 45mm | 400cc | 5.1 | 175 bar | 714
34%
49%
Due to reduced power-pack of the XX-IIS, the hydraulic motor is artificially made smaller to maintain plasticizing speed, at the expense of very low torque (bad for engineering resins)

## Slide 24: Plasticizing Back Pressure Control
Tracking closer to optimal (blue line) better
Precise back pressure control is vital for processing sensitive resins
MK6 almost tracks optimal perfectly, even at low pressure
XX-II/IIS consistently overshoots and cannot achieve low back pressure

## Slide 25: Max. Heater Power
12.9
kW
XX1600IIS
XX1600II
10
kW
11.8
kW
JM168-MK6
Bigger numbers are better
Inadequate heating power reduces plasticizing quality and efficiency, lengthens cycle time
29%

## Slide 26: Clamp Performance
Comparisons of Platen and
Toggle Designs, Specs &
Actual Measurements
INTERNAL ONLY

## Slide 27: Dry Cycle Time
Smaller numbers are better
Look for: smooth motion, no fluctuations, no overshoots
MK6’s toggle mechanism and hydraulic circuit is based on advanced Japanese designs, enabling ultra-high speed operations
XX1600II
XX1600IIS
JM168-MK6
Clamp Speed
Clamp Position
1.9 sec.
3.4 sec. (+80%)
3.5 sec. (+84%)
Japanese Hydraulic
& Mechanical Tech.

## Slide 28: Platen Deformation
Smaller numbers are better
Large deformations can cause flashes
MK6 v.next will target <0.1mm deformation
0.148mm
0.166mm
0.15mm
XX1600II
XX1600IIS
JM168-MK6

## Slide 29: Uniformness of Tie-Bar Deformations
All four tie-bars must deform equally, or uniformly, for the best part quality without flashes and internal stresses
Only MK6’s special toggle design based on advanced Japanese technology guarantees absolute uniformity
XX1600II
XX1600IIS
JM168-MK6
> 10%
1-10%
< 1%
Japanese
Toggle Design

## Slide 30: Bushings for the Moving Platen
XX1600II
XX1600IIS
JM168-MK6
Smooth motion
Low friction
high friction
high friction
Oil-less
Bushings
metallic
metallic

## Slide 31: MK6 – “A4” Mould Protection Feature
MK6 delivers the ultimate in mould protection – a single sheet of A4 paper, at 99% clamp speed and pressure settings
Precision Hydraulics® at works here
XX-II/IIS has no equivalent mould protection feature
Place sheet of A4 paper inside clamp
Close clamp at 99% speed & pressure!
Clamp bounces open and alarm sounds
Inspect paper: it is not even punctured through!

## Slide 32: Reopening a Locked Clamp
Locked Period | Model | XX1600II | XX1600IIS | JM168-MK6
1 hour | Pressure | 140 bar | 150 bar | ＜100 bar
 | Status | Large noise Hard vibration | Large noise Hard vibration | Silky Smooth
60 hours | Pressure | 140 bar | 150 bar | ＜100 bar
 | Status | Large noise Hard vibration | Large noise Hard vibration | Silky Smooth

## Slide 33: Opening Stroke
450
mm
XX1600IIS
XX1600II
430
mm
430
mm
JM168-MK6
Bigger numbers are better
Larger opening strokes enable production of deep-cavity parts

## Slide 34: Minimum Mould Height
170
mm
XX1600IIS
XX1600II
180
mm
180
mm
JM168-MK6
Smaller numbers are better
Smaller minimum moulding height enables production of thin-walled parts

## Slide 35: Ejector Force
4.2
ton
XX1600IIS
XX1600II
3.3
ton
3.3
ton
JM168-MK6
Bigger numbers are better
Larger ejector force enables production of deep-cavity/extra-long parts

## Slide 36: Mould Adj. Performance
Comparisons of Specs &
Actual Measurements
INTERNAL ONLY

## Slide 37: Automatic Clamping Force Adjustment
Model | Time Needed | Set Clamp Force | Set Clamping Pressure
JM168-MK6 | 29 sec. |  | not needed
XX1600II | 27 sec. |  | 
XX1600IIS | 28 sec. |  | 
Due to complex non-linear relationship between clamping pressure and clamping force, achieving accurate clamping force usually requires experience and certain “black arts”
MK6 allows intelligent automatic adjustment of clamping force (at the time expense of 1 second), eliminating guess-work and the needs for experts

## Slide 38: Electricals
Comparisons of Specs &
Standards
INTERNAL ONLY

## Slide 39: Low-Voltage Terminals
XX1600II
XX1600IIS
JM168-MK6
CE-standard
spring-type terminals
traditional
terminals
traditional
terminals

## Slide 40: Power Connection Terminals
XX1600II
XX1600IIS
JM168-MK6
CE-compliant terminals
normal terminals
not compliant
to safety regs
normal terminals
not compliant
to safety regs

## Slide 41: Power Pack
Comparisons of Specs
INTERNAL ONLY

## Slide 42: Maxiumum Sustainable Power Output
XX1600II
XX1600IIS
JM168-MK6
Pump: 64cc (Germany)
Servo: Phase, Innovance
Max. power: 22kW
Pump: 50cc (China)
Servo: self-made
Max. power: 15kW
Pump: 64cc (China)
Servo: self-made
Max. power: 15kW
Fast, High Power (22kW)
low power (15kW)
slow, low power (15kW)

## Slide 43: Impact of Maximum Power Output on Application Processes
Power Demand by Process | 5kW | 10kW | 15kW | 20kW
JM168-MK6 |  |  |  | 
XX1600II |  |  | not energy efficient! | trips alarm!
XX1600IIS |  |  | not energy efficient! | trips alarm!
Different applications require different power outputs (e.g. engineering resins and thin-walled parts require more power)
If process power demand exceeds servosystem limit, alarm is tripped and machine stops
Energy efficiency drops significantly when power output is close to limit
Notes: As a servo-pump system can achieve 0 rpm, ACTUAL energy consumption is NOT related to max. power limit