## Slide 1
MK6 vs XX-A5 (Internal Confidential)

## Slide 2: Measured Performance
Specifications vs Actual Measured
INTERNAL ONLY

## Slide 3: Summary Scoring
Model | General | Electricals | Hydraulics | Mechanics | Total Score
JM168-MK6 |  |  |  |  | 16
XX160-A5 |  |  |  |  | 5

## Slide 4: Highest Actual Measured Speed for All Specifications at 99% Settings
 | 单位 | XX160-A5 | JM168-MK6
Max. Clamp Closing Speed | mm/s | 768 | 817 (+6%)
Max. Clamp Opening Speed | mm/s | 1,242 | 1,313 (+6%)
Max. Injection Speed | mm/s | 98 | 108 (+10%)
Max. Plasticizing Speed | rpm | 233 | 224 (-4%)
Max. Mould Adj. Speed | mm/s | 1.7 | 2.5 (+50%)
MK6 has a all-rounded speed advantage
XX-A5 is slightly faster in plasticizing rpm (but at the expense of very low torque due to much smaller hydraulic motor)

## Slide 5: What Makes The Difference
Precision Hydraulics®
for the MK6

## Slide 6: Precision Hydraulics®
Next-Gen computer control algorithms and hydraulics circuit design
Developed by senior Japanese engineers with decades of technical expertise, using advanced hydraulics simulation software
Enhancement of 3rd Gen Servo-Pump technology: from 3G to 4G
Eliminates unnecessary pressure drops for ultimate precision
Precision at HIGH SPEED
(JM168-MK6 has sustainable dry cycle of only 1.9s)
Rock-Solid Stability
(little vibrations and shocks even running at max. speed)
High Repeatability
(tolerances < 0.05%)

## Slide 7: Injection Performance
Comparisons of Injection Specs &
Actual Measurements
INTERNAL ONLY

## Slide 8: Injection Speed Response (0 → 99%)
Injection speed response curves from 0-99%
Smaller numbers are better
Look for: smoothness, no fluctuations, no overshoots
XX160-A5
JM168-MK6
220ms
520ms
Command
Speed
Position

## Slide 9: The Importance of Speedy Response
Time
Speed
JM168-MK6
XX160-A5
220ms
520ms
Notes
Response is similar to a sports car – 0-100kph acceleration time
Smooth rides at high speed demands quick responses
Snappy responses reduce cycle times, increase productivity
Quick responses are particularly beneficial to difficult or thin-walled moulding processes
(0 → 99%)

## Slide 10: Injection Pressure Control
Look for: smoothness, no fluctuations, no overshoots
Injection pressure control is vital to ultimate part quality
Special materials (e.g. engineering resins) are particularly sensitive to pressure fluctuations
Stable injection pressure has a definitive impact on yield rates
MK6 has superior pressure control
XX160-A5
JM168-MK6

## Slide 11: Injection Base Pressure and Pressure Drop
10
XX160-A5
20
JM168-MK6
24
Lose
55%
Smaller numbers are better
Base pressure and pressure drops are non-work wasted energy dispersed as heat, requiring even more energy to cool
High base pressure or pressure drops leads to significantly lower power efficiency and energy saving
MK6’s Precision Hydraulics® all but eliminates pressure drops and has very low base pressure
Pressure
Drop (bar)
Base
Pressure
(bar)
Base
Pressure
(bar)

## Slide 12: Injection Pressure
188
MPa
XX160-A5
163
MPa
JM168-MK6
Bigger numbers are better
Higher injection pressure means better and more consistent part quality
15%

## Slide 13: Nozzle Protection Guard
XX160-A5
JM168-MK6
Easy to operate
not convenient
Window
no window

## Slide 14: Injection Carriage Cylinders
XX160-A5
JM168-MK6
Easy to operate on nozzle
not convenient when working on nozzle
Diagonal
Dual Balanced
horizontal dual
balanced

## Slide 15: Injection Base
XX160-A5
JM168-MK6
Smoothness for
high-speed injection
not designed for
high-speed injection
Linear Rails
traditional guide rods

## Slide 16: Holding Performance
Comparisons of Holding Specs &
Actual Measurements
INTERNAL ONLY

## Slide 17: Holding Pressure Response (0 → 99%)
Holding pressure response curves from 0-99%
Smaller numbers are better
Look for: smoothness, no fluctuations, no overshoots
Stable holding pressure is vital to part quality and high yield
XX-A5 experiences significant overshoots and instabilities
XX160-A5
JM168-MK6
270ms
490ms
Cmd.
Pres.

## Slide 18: Pressure Control
Look for: smoothness, no fluctuations, no overshoots
XX-II/IIS have lower quality pressure control – i.e. high fluctuations and overshoots
MK6’s innovative Precision Hydraulics® technology yields precise pressure control
Precise pressure control is vital for demanding, pressure-sensitive applications such as optical parts
XX160-A5
JM168-MK6

## Slide 19: V/P Switch-Over Response
Look for: smoothness, no fluctuations, no overshoots
Precise and stable V/P switch-over is vital for demanding applications requiring precise dosing
XX160-A5
JM168-MK6
Patented
Technology
Injection Command
Actual Pressure
Pressure Command

## Slide 20: Back Pressure Control
XX160-A5
JM168-MK6
Easy, fast, accurate
not convenient slow and inaccurate
Digital
manual

## Slide 21: Plasticizing Performance
Comparisions of Specs &
Actual Measurements
INTERNAL ONLY

## Slide 22: Plasticizing Motor Size and Torque
XX160-A5
JM168-MK6
Size: 500cc
Unit torque: 80 Nm
Size: 400cc
Unit torque: 56 Nm
Fast and Strong
weak!

## Slide 23: Plasticizing Torque
Model | Screw Diam. | Flow Rate | Unit Torque | Max. Pressure | Max. Torque
JM168-MK6 | 46mm | 500cc | 8 | 175 bar | 1,400
XX160-A5 | 48mm | 400cc | 5.6 | 175 bar | 980
30%
Due to reduced power-pack of the XX-A5, the hydraulic motor is artificially made smaller to maintain plasticizing speed, at the expense of very low torque (bad for engineering resins)

## Slide 24: Max. Heater Power
12.9
kW
XX160-A5
10.9
kW
JM168-MK6
Bigger numbers are better
Inadequate heating power reduces plasticizing quality and efficiency, lengthens cycle time
18%

## Slide 25: Clamp Performance
Comparisons of Platen and
Toggle Designs, Specs &
Actual Measurements
INTERNAL ONLY

## Slide 26: Space Between Tie-bars
XX160-A5
JM168-MK6
470 mm
460 mm
460 mm
470 mm

## Slide 27: Dry Cycle Time
Smaller numbers are better
Look for: smooth motion, no fluctuations, no overshoots
MK6’s toggle mechanism and hydraulic circuit is based on advanced Japanese designs, enabling ultra-high speed operations
XX160-A5
JM168-MK6
Clamp Speed
Clamp Position
1.9 sec.
2.7 sec.
(+42%)
Japanese Hydraulic
& Mechanical Tech.

## Slide 28: Platen Construction
XX160-A5
JM168-MK6
Solid inside
Actual thickness: 142 mm
Hollow inside
Actual thickness: 70mm
No Deformation
large deformation

## Slide 29: Platen Deformation
Smaller numbers are better
Large deformations can cause flashes
MK6 v.next will target <0.1mm deformation
0.314mm
0.15mm
XX160-A5
JM168-MK6

## Slide 30: Uniformness of Tie-Bar Deformations
All four tie-bars must deform equally, or uniformly, for the best part quality without flashes and internal stresses
Only MK6’s special toggle design based on advanced Japanese technology guarantees absolute uniformity
XX160-A5
JM168-MK6
> 10%
1-10%
< 1%
Japanese
Toggle Design

## Slide 31: Bushings for the Moving Platen
XX160-A5
JM168-MK6
Smooth motion
Low friction
high friction
Oil-less
Bushings
copper

## Slide 32: Lubrication Oil Sensor
XX160-A5
JM168-MK6
Sensor installed at application end
sensor installed at pump limited detection
Perfect Detection
poor detection

## Slide 33: MK6 – “A4” Mould Protection Feature
MK6 delivers the ultimate in mould protection – a single sheet of A4 paper, at 99% clamp speed and pressure settings
Precision Hydraulics® at works here
XX-II/IIS has no equivalent mould protection feature
Place sheet of A4 paper inside clamp
Close clamp at 99% speed & pressure!
Clamp bounces open and alarm sounds
Inspect paper: it is not even punctured through!

## Slide 34: Reopening a Locked Clamp
Locked Period | Model | XX160-A5 | JM168-MK6
1 hour | Pressure | >150 bar | ＜100 bar
 | Status | Large noise Hard vibration | Silky Smooth
60 hours | Pressure | >160 bar | ＜100 bar
 | Status | Large noise Hard vibration | Silky Smooth

## Slide 35: Hydraulic Safety Valve
XX160-A5
JM168-MK6
Compliant to all safety standards
no safety valve not compliant to safety regulations

## Slide 36: Opening Stroke
450
mm
XX160-A5
420
mm
JM168-MK6
Bigger numbers are better
Larger opening strokes enable production of deep-cavity parts

## Slide 37: Ejector Force
4.2 吨
XX160-A5
4.2 吨
JM168-MK6
Bigger numbers are better
Larger ejector force enables production of deep-cavity/extra-long parts

## Slide 38: Mould Adj. Performance
Comparisons of Specs &
Actual Measurements
INTERNAL ONLY

## Slide 39: Automatic Clamping Force Adjustment
Model | Time Needed | Set Clamp Force | Measure Mould Thickness
JM168-MK6 | 29 sec. |  | not needed
XX160-A5 | 77 sec. |  | Must
Due to complex non-linear relationship between clamping pressure and clamping force, achieving accurate clamping force usually requires experience and certain “black arts”
Both allow intelligent automatic adjustment of clamping force
XX-A5 also requires measuring the mould’s actual thickness which is time-consuming

## Slide 40: Electricals
Comparisons of Specs &
Standards
INTERNAL ONLY

## Slide 41: Electrical Cabinet
XX160-A5
JM168-MK6
Galvanized sheet
traditional resin board
Resistant to
Interference
prone to interference

## Slide 42: Low-Voltage Terminals
XX160-A5
JM168-MK6
CE-standard
spring-type terminals
traditional
terminals

## Slide 43: Power Connection Terminals
XX160-A5
JM168-MK6
CE-compliant terminals
normal terminals
not compliant
to safety regs

## Slide 44: Safety Modules
XX160-A5
JM168-MK6
Pilz (Germany) Fully compliant to
safety standards
no safety module
not compliant to safety regulations

## Slide 45: Nozzle Guard Safety Switch
XX160-A5
JM168-MK6
Full Compliant to
Safety Standards
no safety switch
not compliant to safety regulations

## Slide 46: Guard Door Safety Switches
XX160-A5
JM168-MK6
Safety Switch Full Compliant to
Safety Standards
non-safe switch
not compliant to safety regulations

## Slide 47: Power Pack
Comparisons of Specs
INTERNAL ONLY

## Slide 48: Maxiumum Sustainable Power Output
XX160-A5
JM168-MK6
Pump: 64cc
Max. power: 22kW
Pump: 50cc
Max. power: 17.5kW
Fast, High Power (22kW)
slow, low power (15kW)

## Slide 49: Impact of Maximum Power Output on Application Processes
Power Demand by Process | 5kW | 10kW | 15kW | 20kW
JM168-MK6 |  |  |  | 
XX160-A5 |  |  |  | trips alarm!
Different applications require different power outputs (e.g. engineering resins and thin-walled parts require more power)
If process power demand exceeds servosystem limit, alarm is tripped and machine stops
Energy efficiency drops significantly when power output is close to limit
Notes: As a servo-pump system can achieve 0 rpm, ACTUAL energy consumption is NOT related to max. power limit