# Chen Hsong CH-3.5 PC Computer Controller

  - Characteristics

  - Basic Features

  - Introduction to the Computer Panel

3.3.1		The Computer Panel Layout

3.3.2		Temperature Control Keys

3.3.3		Moulding Parameter Control Keys

3.3.4		Manual Control Keyboard

3.3.5		Power Switch

3.4	Operation of screen

3.4.1		Mains Start Up Inspection					Screen (00)

3.4.2		Operation and Temperature Setting				Screen (01-03)

3.4.3		Temperature Deviation Alarm Setting			Screen (04)

3.4.4		Mould Clamping Setting						Screen (05)

3.4.5		Mould Opening Setting						Screen (06)

3.4.6		Ejector Setting								Screen (07)

3.4.7		Core Pulling 1 Setting						Screen (08)

3.4.8		Core Pulling 2 Setting						Screen (09)

3.4.9		Core Pulling 3 Setting						Screen (10)

3.4.10		Unscrewing 1 Setting						Screen (11)

3.4.11		Unscrewing 2 Setting						Screen (12)

3.4.12		Injection Setting							Screen (13)

3.4.13		Plasticization Setting						Screen (14)

3.4.14		Mould Thickness and Clamping Force Setting	Screen (15)

3.4.15		Injection Unit Movement Setting				Screen (16)

3.4.16		Function Selection Setting					Screen (17)

3.4.17		Lubrication Setting							Screen (18)

3.4.18		Counter Setting							Screen (19)

3.4.19		Timer Setting								Screen (20)

3.4.20		Timer Setting								Screen (21)

3.4.21		Adjustment Function Setting					Screen (22)

3.4.22		Mould Number Selection Setting				Screen (23)

3.4.23		Mould Number Copying Setting				Screen (24)

3.4.24		Quality Statistics							Screen (25)

3.4.25		Injection Ending Position Graphic Display		Screen (26)

3.4.26		Pressure Switch Setting						Screen (27)

3.4.27.1	Initial Position Setting						Screen (28)

      - The Procedure for Resetting of the Initial

Position after a Sudden Power Failure of

the Computer

      - Description on the Encode Initial Position

Setting Screen

3.4.28	Ramp Up/Down Setting						Screen (29)

3.4.29.1	Auxiliary Speed and Pressure Setting			Screen (30)

3.4.29.2	Auxiliary Speed and Pressure Setting			Screen (31)

3.4.29.3	Auxiliary Speed and Pressure Setting			Screen (32)

3.4.30	Ladder Program Monitoring					Screen (33)

3.4.31	Input/Output Monitoring						Screen (34, 35, 36, 37,

38, 39)

3.4.32	Input/Output Status Monitoring Screen			Screen (40, 41)

3.4.33	Timer Monitoring Screen					Screen (42, 43)

3.4.34	Counter Monitoring Screen					Screen (44)

3.4.35	Language Selection and Memory Erase			Screen (45)

3.4.36	Speed Linearization							Screen (46)

3.4.37	Pressure Linearization						Screen (47)

3.4.38	Speed and Pressure Adjustment				Screen (48)

3.4.39	Air Blow Setting							Screen (49)

3.5	Alarm Message and Trouble Shooting

3.5.1		Description of Computer Warning Message

3.5.2		Description of Alarm Message of System Faults

3.5.3		Description of Title of Faults

## Moulding Operation Instruction

3.6.1		Temperature Control Setting

3.6.2		Setting of the Temperature Deviation (alarm)

3.6.3		Setting of the Temperature Preheat Function

3.6.4		Selection of Fully Automatic, Semi-Automatic or Manual Operation

3.6.5		Setting of Position, Speed and Pressure Data

3.6.6		Setting of the Numeric Data for Moulding Conditions

3.6.7		Adjustment of Proportional Numerical Control

3.6.8		Enable and Disable the Key Lock Function

3.6.9		Description of Application of the Computer’s Internal Counters

3.6.10		Description of Application of the Computer’s Internal Timer

3.6.11		Description of Input and Output Port of the Computer

3.7	CH-3.5PC Special Screen Operation

3.8		CH-3.5PC Standard Electrical Wiring Diagram

  - Characteristics

The Chen Hsong CH-3.5 PC computer controller is manufactured in Japan to JIS standards of manufacture and inspection. It features a 300-character, Chinese language, extra-large LCD screen. The operating voltage range is AC 110V~AC 280V 50/60 Hz. It is of high stability. The data stored may be kept for 5 years or above under the condition of power failure. Hence it is safe and reliable. Chinese, English and Japanese language can be freely selected and they can be switched over from one to the other, facilitating easy learning of the computer operation.

### Basic Features

- Enlarged memory which may store 150 sets of mould information ( e.g. time, counting times, pressure, speed, stroke, quantity, mould thickness, explanation of mould No., conditions for selection, barrel temperature. )

- Data Lock function prevents unauthorized access and mistaken amendments.

- Automatic setting of high-pressure clamping position values.

- Setting of the heating time for the nozzle with up to 100% temperature being maintained.

- Temperature may be adjusted and controlled within the range of 30℃—500℃ through temperature PID and the thermocouple temperature sensing line is of the K type.

- Cold start prevention, automatic preheat function.

- High temperature and low temperature alarm setting and breakage of the thermocouple cable alarms.

- Automatic detection of blocked nozzle and material overflow.

- 5 stage injection speeds, 5 stage injection pressure and 2-stage holding pressures.

- 2 stage plasticizing speed and 2 stage plasticizing pressure.

- High-accuracy encoder used for mould-locking, injection and ejection.

- Data input error prevention and prompting.

- Production volume setting for auto-stop function.

- Lubrication setting for the toggle unit, setting the frequency of lubrication for mechanical links and an alarm for low oil level.

- Operation display.

- Diagnostic function can check the status of inputs and outputs and monitors the timers and counters.

- Mould data can be copied or deleted freely. Also by using the mould data copy function in block form from standard mould data, saves on setting times.

- Both the mold data and quality data can be captured by any IBM comptabile PC via a serial communication port with additional software running in Windows 95 system. All this data can be stored on harddisk and printed out by a windows supporting printer.

  - Introduction to the computer panel

3.3.1	The Computer Panel Layout

3.3.2	Temperature Control Keys

This keyboard controls the setting and changing of the temperature display screen.

    - Moulding Parameter Control Keys

This keyboard has the following functions:

- Selecting the moulding operation mode.

- Setting moulding parameters such as position, speed, pressure, time and counters.

- Setting the data needed for automatic mould height adjustment.

- Changing the mould number and copying mould data.

- Selecting the moulding functions and movement in accordance with the requirements of the product and mould design.

- Moving the cursor to change the desired data in any functional screen.

Moulding control parameter keyboard

This keyboard has the following functions:

- Entering the required numerical data for the moulding conditions

Speed setting			00-99, 00 means no speed

Pressure setting		00-99, 00 means no pressure

Position setting		0000-999.9 mm

Time setting			0-6553.5 sec

Counter setting		0-65535

Mould thickness setting	0-6553.5 mm

- Checking if the keyboard is operating normally

- Accessing out the computer control program

(4)		Checking the operating status of outputs, inputs and timers.

3.3.4	Manual Control Keyboard

- The manual operation keyboard can be used to operate the individual movements of the moulding cycle.

- Mould height adjustment and automatic door operation use the same key as the mould height adjustment function. The screen display must be mould height adjustment.

3.3.5	Power Switch

- Emergency Stop Button

The red button at the lower right hand corner of the computer panel is used to cut off the electrical supply when it is pressed. Before restarting the machine, turn the red button according to the direction of arrows to unlock the button.

- Power ON Push Button

The green Power ON Push Button is located below the red Emergency Stop Button on the computer panel. When it is pressed, the power supply control unit of this machine will be turned on. This function will protect the computer system effectively, when power is suddenly turned off.

- The computer includes a voltage stabilizer unit for power input. This will maintain its normal function if the power input varies within the range of AC 90V-AC 265V 50/60 Hz.

  - Operation Screen

    - Mains start up inspection

Mains start up screen (00)

CHEN HSONG MACHINERY TEL ﹕ 852-26653222 FAX ﹕ 852-26641115 MODEL ﹕ JM80MKIV SERIAL NO. ﹕ DATE ﹕ 1999-9-1 PROGRAM ﹕ ABCDE CHECK SAFETY DEVICE BEFORE OPERATE DISP : 6 CTRL : 4

- After switched on the machine, the system performs a self-test and also displays screen (00). This screen shows the machine model, serial number and program used. After 3 seconds the screen will changeover to “Operation screen (01)” automatically.

- When the machine requires repairing or servicing, or for any other technical inquiry, please inform our Customer Service Department  “the machine model, serial no and program used” as shown on this screen.

3.4.2	Operation and temperature setting

During manual operation, the screen (01) is shown as below:

T1		T2		T3		T4		T5		T6		T7		T8

AA		BB		CC		DD		EE		FF		GG	　	HH		WR

II		??		??		??		??		??		??	　	??		RD

OFF		NOZZ	JJ %

MOLD　﹕12

???bar			????p			??? mm			???? mm

During automatic operation, the screen (02) is shown as below:

T1		T2		T3		T4		T5		T6		T7		T8

AA		BB		CC		DD		EE		FF		GG	　	HH		WR

II		??		??		??		??		??		??	　	??		RD

OFF		NOZZ	JJ %

MOLD　﹕12

???bar			????p			??? mm			???? mm

The screen (03) is shown as below

T1		T2		T3		T4		T5		T6		T7		T8

AA		BB		CC		DD		EE		FF		GG	　	HH		WR

II		??		??		??		??		??		??	　	??		RD

JJ		NOZZ	KK %

AUTO

FILLING		LL	s					INJ.			MM	s

CYC. TIME	NN	s					COOL		OO	s

CYCLE NO	PP	t					RECYC.		QQ	s

MOLD　﹕12

???bar			????p			??? mm			???? mm

Press  to display Screen (02), press  again to display Screen (03). The screen (02) and screen (03) can change regularly.

In which the items are:

" I	I "	: 	In display of the data measured by the computer

"KK"	: 	Nozzle heating the proportional value setting

"AA"	: 	Zone 1 temperature setting

"BB"	: 	Zone 2 temperature setting

"CC"	: 	Zone 3 temperature setting

"DD"	: 	Zone 4 temperature setting

"EE"	: 	Zone 5 temperature setting (depends on the machine clamp tonnage)

"FF"	: 	Zone 6 temperature setting (depends on the machine clamp tonnage)

"GG"	: 	Zone 7 temperature setting (depends on the machine clamp tonnage)

"HH"	: 	Zone 8 temperature setting (depends on the machine clamp tonnage)

"JJ"	:	Temperature mode Setting switch. By pressing the key  or

one of the three modes will be selected

(ON, OFF, PREHEAT)

"LL"	: 	Injection filling time display

"MM"	: 	Injection time setting

"NN"	: 	Automatic cycle time display

"OO"	: 	Cooling time setting

"PP"	: 	No. of moulding produced display

"QQ"	: 	Recycle time setting

Under automatic operation mode, the injection time, cooling time or recycle time can be changed during this screen display by moving the cursor to the appropriate position and pressing the numerical keys to enter the required figures and then pressing “Input” to change the setting

(1)	To change the temperature setting, in the screen (01), (02) and (03) and depending on the stage of which the temperature is to be changed:

(2) 	Press   or    or    or

or    or    or    or    or

the cursor will appear on the screen.

(3) 	Press the “Cursor” key  to select the setting for the corresponding

temperature stage. Key in the numerical data and press  to complete

the setting.

3.4.3	Temperature Deviation Alarm Setting

Temperature deviation alarm setting screen (04)

T1		T2		T3		T4		T5		T6		T7		T8

AA		BB		CC		DD		EE		FF		GG	　	HH		WR

II		??		??		??		??		??		??	　	??		RD

JJ		NOZZ	KK %

ALARM

HI		+LL		+MM	+NN		+OO		+PP		+QQ		+RR		+SS

LO		-TT		-UU		-VV		-WW	-XX		-YY		-ZZ		-AB

PREHEAT RATIO				AC	%

NOZZLE HEATING CYCLE		AD	s

???bar			????p			??? mm			???? mm

(1)	Press                                                                       and    simultaneously to display screen (04)

(2)	Press the Cursor key       to select the temperature deviation alarm

setting values for all stages. Press the numerical keys to enter the required values and

complete the setting by pressing        again.

Shown on the screen:

"JJ	"	:	Temperature control        or          mode selection to

select the following three modes :

(i)	ON

(ii)	OFF

(iii)	PREHEAT

"LL"	: 	Zone 1 temperature deviation high limit alarm setting

"MM"	: 	Zone 2 temperature deviation high limit alarm setting

"NN"	: 	Zone 3 temperature deviation high limit alarm setting

"OO"	:	Zone 4 temperature deviation high limit alarm setting

"PP"		: 	Zone 5 temperature deviation high limit alarm setting

"OO"	: 	Zone 6 temperature deviation high limit alarm setting

"RR"	:	Zone 7 temperature deviation high limit alarm setting

"SS"		: 	Zone 8 temperature deviation high limit alarm setting

"TT"	: 	Zone 1 temperature deviation low limit alarm setting

"UU"	: 	Zone 2 temperature deviation low limit alarm setting

"VV"	: 	Zone 3 temperature deviation low limit alarm setting

"WW"	: 	Zone 4 temperature deviation low limit alarm setting

"XX"	: 	Zone 5 temperature deviation low limit alarm setting

"YY"	: 	Zone 6 temperature deviation low limit alarm setting

"ZZ"	: 	Zone 7 temperature deviation low limit alarm setting

"AB"	: 	Zone 8 temperature deviation low limit alarm setting

"AC"	: 	During preheat, (%) temperature reduction setting

"AD"	:	Nozzle temperature cycle time setting:

3.4.4	Mould Clamping Setting

Mould clamping Setting Screen (05)

CLAMPING

SP			PR					POSIT.

FAST CLA		AA %		BB %		TO		CC mm

L.P. LOCK		DD %		EE %		TO		FF p

H.P. LOCK		GG %		HH %		TO		II p

CLAMP AUX								AT		JJ mm

CLAMPING FORCE:			KK TON				LL p

???bar			????p		??? mm			???? mm

- Press                or           or      to display screen (05).

(2)	Press the Cursor key        to select the mould-clamping parameter settings.

Press the numerical keys to enter the required figures and then press

to complete the setting

Shown on the screen:

“AA"	:	Fast mould clamping speed setting

"BB"	:	Fast mould clamping pressure setting

"CC"	:	Fast mould clamping end position setting

"DD"	:	Low-pressure mould clamping speed setting

"EE"	:	Low-pressure mould clamping pressure setting

"FF"		:	Low-pressure mould clamping end position

At manual mode, carry out mould clamping until the mould reaches the

closed position at which the toggle is not fully extended , then press

and        together , the high pressure mould clamping start position (FFp

valve) will be automatically set.

"GG"	:	High pressure mould clamping speed setting

"HH"	:	High pressure mould clamping pressure setting

"II"		:	High-pressure mould clamping end position setting

"JJ"		:	Mould clamping auxiliary position setting (optional function )

"KK"    :	Clamping force in tons. This value is calculated automatically from the position (FF p).

(It is only a value for reference and not an absolute value)

Low Pressure Stroke Alarm

(TIM 6)

AA %   BB%           DD %   EE %             GG %   HH %

Fast mould closing       Low pressure clamping       High pressure clamping

CC mm                         FF p                 II p

3.4.5	Mould-opening setting

Mould Opening Setting Screen (06)

OPENING

SP			PR					POSIT

BREAK			AA %		BB %		TO		CC p

FAST OPEN		DD %		EE %		TO		FF mm

SLOW OPEN		GG %		HH %		TO		II mm

OPEN AUX								AT		JJ mm

MAXIMUM OPENING STROKE						KK mm

???			????			??? mm			???? mm

(1)	Press          or                     or         to display screen (06)

(2)	Press the cursor key         to select the mould-opening parameter

item settings.

Press the numerical keys to enter the required figures and then press

to complete the setting.

Shown on the screen:

"AA"	: 	Break speed setting

"BB"	: 	Break pressure setting

"CC"	: 	Break end position setting

"DD"	: 	Fast mould open speed setting

"EE"		:	Fast mould open pressure setting

"FF"		: 	Fast mould open end position setting

"GG"	: 	Setting of speed for reduced-speed mould-opening

"HH"	: 	Setting of pressure for reduced-speed mould-opening

"II"	: 	Setting of the end position for the action of reduced-speed

mould-opening

"JJ"	: 	Setting of the position of the standby mould-opening

action (optional function or air blowing position during mould-opening)

"KK"	 : 	Displayed max. mould-opening stroke

GG %   HH %        DD %   EE %        AA %  BB %

Reduced speed mould open    Fast mould open       Slow mould open

↑                       ↑                   ↑

II mm                   FF mm               CC mm

3.4.6	Ejector Setting

Ejector Setting Screen (07)

EJECTOR

NOS.OFEJE		AA				VIBRATION		BB

MAX.STRK.		CC mm			PAUSE			DD s

EJECT.START.AT OPEN POSIT.						EE mm

EJECTOR MODE	FF

SP			PR					POSIT

EJT.OUT→	GG %		HH %		→		II mm

EJT.IN	←	JJ %			KK %		←		LL mm

???bar			????p		??? mm			???? mm

(1)		Press the key  to display screen (07).

(2)		Press the cursor key         to select the ejector parameter settings.

Press the numerical keys to enter the required figures and then press

to complete setting.

Shown on the screen:

"AA"	:	The number of ejection setting (CNT 04)

"BB"	: 	The number of ejector vibration setting (used with

multiple ejection)  (CNT 05)

"CC"	: 	Maximum ejection stroke display

"DD"	: 	Ejector stopping time (used with ejector stopping at end

of stroke mode) (TIM 11)

"EE"		:	Mould opening position setting for start of ejector during

mould opening stroke (optional function)

"FF"			:	Ejector motion mode. Use                    to

select one of the following three modes,

(i)	No motion

(ii)	Ejector stopping at end of stroke

- Multiple ejection

"GG"	: 	Ejector forward speed setting

"HH"	: 	Ejector forward pressure setting

"II"		: 	Ejector forward motion end position setting

"JJ"		: 	Ejector backward speed setting

"KK"	: 	Ejector backward pressure setting

"LL"		: 	Ejector backward motion changeover position setting

GG %     HH %

Ejector forward

←       LL mm      →

Ejector retract (2)          JJ %   KK %

Speed / pressure          Ejector backward     ↑

(Screen 29)                                II mm

3.4.7	Core Pulling 1 Setting

Core Pulling 1 Setting Screen (08)

CORE IN/OUT 1

CORE1 IN POS.			AA				BB mm

CORE1 OUT POS.			CC				DD mm

CORE1 STOPPER BY		EE

SP			PR				TIME

CORE1 IN	FF %		GG %		→	HH秒

CORE1 OUT	II %		JJ %		←	KK秒

???bar			????p		??? mm			???? mm

(1)	Press       to display Screen (08)

(2)	Press the cursor key  to select the core-pulling parameter

settings.

Press the numerical keys to enter the required figures and then press

to complete setting.

Shown on the screen

"AA"		: 	Core in motion selection	 : press

to select one of the following four modes:

(1)	Before mould clamping

(2)	After mould clamping

(3)	Clamp to;

(4)	Not use

"BB"	: 	It is effective only when Mode (3) “clamp to ” is selected.

It is used to specify the position to start the core in motion.

"CC"  	:	Core out motion selection:  press

to select one of the following four modes:

(i)	Before mould opening

(ii)	After mould opening

(iii)	Open to

(iv)	Not use

"DD"	: 	It’s effective only when mode (3) “open to” is selected. It

is used to specify the position to start the core out motion.

"EE"		:	The core pulling stroke control mode.

Press          to select one of

flowing two mode:

- Limit switch setting (The core in / out stroke is controlled by limit switch)

- Timer setting (The core in / out stroke is controlled by the timer)

"FF"		: 	Core in speed setting

"GG"	: 	Core in pressure setting

"HH"	: 	Core in motion time setting

"II"		: 	Core out speed setting

"JJ"		: 	Core out pressure setting

"KK"	:	Core out motion time setting

3.4.8	Core Pulling 2 Setting

Core Pulling 2 Setting Screen (09)

CORE IN/OUT 2

CORE2 IN POS.			AA				BB mm

CORE2 OUT POS.			CC				DD mm

CORE2 STOPPED BY		EE

SP			PR				TIME

CORE2 IN	FF %		GG %		→	HH s

CORE2 OUT	II %			JJ %			←	KK s

???			????			??? mm			???? mm

(1)		Press  to display screen (09)

(2)		Press the cursor key        to select the core-pulling parameter settings.

Press the numerical keys to enter the required figures and press       to complete setting.

Shown on the screen

"AA"	:	Core in motion selection : Press

to select one of the following four modes.

(1)	Before clamping

(2)	After clamping

(3)	Clamp to;

(4)	Not use

"BB"	: 	It is effective only when Mode (3) “clamp to ” is selected.

It is used to specify the position to start the core in

motion.

"CC"	:	Core out motion selection : press

to select one of the following four modes:

(1)	Before mould opening

(2)	After mould opening

(3)	Open to

(4)	Not use

"DD"	: 	It’s effective only when mode (3) “open to” is selected. It

is used to specify the position to start the core out motion.

"EE"	:	The core pulling stroke control mode. Press

to select one of following two mode:

- Limit switch setting (The core in / out stroke is controlled by limit switch)

- Timer setting (The core in / out stroke is controlled by the timer)

"FF"		:	Core in speed setting

"GG"	: 	Core in pressure setting

"HH"	: 	Core in motion time setting

"II"		: 	Core out speed setting

"JJ"		: 	Core out pressure setting

"KK"	:	Core out motion time setting

3.4.9	Core Pulling 3 Setting

Core Pulling 3 Setting Screen (10)

CORE IN/OUT 3

CORE3 IN POS.			AA				BB mm

CORE3 OUT POS.			CC				DD mm

CORE3 STOPPED BY		EE

SP			PR				TIME

CORE3 IN	FF %		GG %		→	HH s

CORE3 OUT	II %			JJ %			←	KK s

???			????			??? mm			???? mm

(1)		Press  to display screen (10)

(2)	Press the cursor key  to select the core-pulling parameter settings.

Press the numerical keys to enter the required figures and press       to complete setting.

Shown on the screen

"AA"	:	Core in motion selection : Press

to select one of the following four modes.

(1)	Before clamping

(2)	After clamping

(3)	Clamp to;

(4)	Not use

"BB"	: 	It is effective only when Mode (3) “clamp to ” is selected.

It is used to specify the position to start the core in

motion.

"CC"	:	Core out motion selection : press

to select one of the following four modes:

(1)	Before mould opening

(2)	After mould opening

(3)	Open to

(4)	Not use

"DD"	: 	It’s effective only when mode (3) “open to” is selected. It

is used to specify the position to start the core out motion.

"EE"	:	The core pulling stroke control mode. Press

to select one of following two mode:

- Limit switch setting (The core in / out stroke is controlled by limit switch)

- Timer setting (The core in / out stroke is controlled by the timer)

"FF"		:	Core in speed setting

"GG"	: 	Core in pressure setting

"HH"	: 	Core in motion time setting

"II"		: 	Core out speed setting

"JJ"		: 	Core out pressure setting

"KK"	:	Core out motion time setting

3.4.10	Unscrewing 1 Setting

Unscrewing Setting (11)

UNSCREWING1

SCREWING1 POS.			AA						BB

UNSCREW1 POS.			CC						DD

SCREW1 STOP BY			EE

SLOW		FAST		PR			TIME

SCREW1		FF %		GG %		HH %		II

UNSCR1		KK %		LL %		MM %		NN

S.SCREW1		PP s

S.UNSCR1		QQ s

???bar			????p		??? mm			???? mm

(1)	Press  to display screen (11)

(2)	Press the cursor key  to select the unscrewing parameter settings.

Press the numerical keys to enter the required figures and then press

to complete setting.

Shown on the screen

"AA" 	:	Unscrewing forward motion selection : press

to select the one of the following r modes:

(1)	Before mould clamping

(2)	After mould clamping

(3)	clamp to

(4)	Not use

"BB"  :	It’s effective only when mode (3) “clamp to” is selected. It

is used to specify the position to start the unscrewing

forward motion.

"CC" 	:  Unscrewing backward motion selection : press        or

to select one of the following four modes:

(1)	Before mould-opening

(2)	After mould-opening

(3)	Open to

(4)	Not use

"DD" 	: 	It’s effective only when mode (3) “open to” is selected. It

is used to specify the position to start the unscrewing

backward motion.

"EE"  :		Unscrewing stroke control mode: press   or           to select one of the two modes:

(1)	Limit switch setting (The unscrewing stroke is controlled by limit switch)

(2)	Timer setting (The unscrewing stroke is controlled by timer)

"FF"	:	Unscrewing forward slow speed setting

"GG"	:	Unscrewing forward fast speed setting

"HH"	:	Unscrewing forward pressure setting

"II"	:	Unscrewing forward motion time setting (unscrewing

forward motion is terminated by the timer)

"JJ"		:	Unscrewing forward motion count setting (unscrewing

forward motion is terminated by the counter)

"KK"	:	Unscrewing backward slow speed setting

"LL"	:	Unscrewing backward fast speed setting

"MM"	:	Unscrewing backward pressure setting

"NN"	:	Unscrewing backward motion time setting (unscrewing

backward motion is terminated by the timer)

"OO"	:	Unscrewing forward motion counter setting (unscrewing

backward motion is terminated by the counter)

"PP"	:	Unscrewing forward slow speed time setting

"QQ"	:	Unscrewing backward slow speed time setting

3.4.11	Unscrewing 2 Setting

Unscrewing Setting (12)

UNSCREWING2

SCREWING2 POS.			AA						BB

UNSCREW2 POS.			CC						DD

SCREW2 STOP BY			EE

SLOW		FAST		PR			TIME

SCREW2		FF %		GG %		HH %		II

UNSCR2		KK %		LL %		MM %		NN

S.SCREW2		PP s

S.UNSCR2		QQ s

???bar			????p		??? mm			???? mm

(1)	Press  to display screen (12)

(2)	Press the cursor key  to select the unscrewing parameter settings.

Press the numerical keys to enter the required figures and then press

to complete setting.

.

Shown on the screen

"AA" 	:	Unscrewing forward motion selection : press

to select the one of the following r modes:

(1)	Before mould clamping

(2)	After mould clamping

(3)	clamp to

(4)	Not use

"BB"  :	It’s effective only when mode (3) “clamp to” is selected. It

is used to specify the position to start the unscrewing

forward motion.

"CC" 	:  Unscrewing backward motion selection : press        or

to select one of the following four modes:

(1)	Before mould-opening

(2)	After mould-opening

(3)	Open to

(4)	Not use

"DD" 	: 	It’s effective only when mode (3) “open to” is selected. It

is used to specify the position to start the unscrewing

backward motion.

"EE"  :		Unscrewing stroke control mode: press   or           to select one of the two modes:

(1)	Limit switch setting (The unscrewing stroke is controlled by limit switch)

(2)	Timer setting (The unscrewing stroke is controlled by timer)

"FF"	:	Unscrewing forward slow speed setting

"GG"	:	Unscrewing forward fast speed setting

"HH"	:	Unscrewing forward pressure setting

"II"	:	Unscrewing forward motion time setting (unscrewing

forward motion is terminated by the timer)

"JJ"		:	Unscrewing forward motion count setting (unscrewing

forward motion is terminated by the counter)

"KK"	:	Unscrewing backward slow speed setting

"LL"	:	Unscrewing backward fast speed setting

"MM"	:	Unscrewing backward pressure setting

"NN"	:	Unscrewing backward motion time setting (unscrewing

backward motion is terminated by the timer)

"OO"	:	Unscrewing forward motion counter setting (unscrewing

backward motion is terminated by the counter)

"PP"	:	Unscrewing forward slow speed time setting

"QQ"	:	Unscrewing backward slow speed time setting

3.4.12	Injection Setting

Injection Setting Screen (13)

INJECTION					MODE　﹕XX

FILLING		AA秒		CUSHION		BB	mm

INJ. TIME	CC秒		SCREW END		DD	mm

SP			PR				POSIT.

INJECT 1				EE %		FF %	TO		GG	mm

INJECT 2				HH %		II %		TO		JJ	mm

INJECT 3				KK %		LL %	TO		MM	mm

INJECT 4				NN %		OO %	TO		PP	mm

INJECT 5				QQ %		RR %	UPTO	SS	mm

HOLDING1			TT %		TIME			UU	s

HOLDING2			VV %		TIME			WW	s

???bar		????p		??? mm			???? mm

(1)	Press  or or  to display screen (13)

(2)	Press the cursor key  to select the injection parameter settings.

Press the numerical keys to enter the required figures and then press

to complete setting.

Shown on the screen,

"AA"	:	Injection 1st to 4th stage time display

"BB"	:	Injection display

"CC"	:	Injection time setting

"DD"	:	Plasticizing end position setting

"EE"		:	Injection Stage 1 speed setting

"FF"		:	Injection Stage 1 pressure setting

"GG"	:	Injection Stage 1 end position setting

"HH"	:	Injection Stage 2 speed setting

"II"		:	Injection Stage 2 pressure setting

"JJ"		:	Injection Stage 2 end position setting

"KK"	:	Injection Stage 3 speed setting

"LL"		: 	Injection Stage 3 pressure setting

"MM"	: 	Injection Stage 3 end position setting

"NN"	: 	Injection Stage 4 speed setting

"OO"	: 	Injection Stage 4 pressure setting

"PP"		: 	Injection Stage 4 end position setting

"QQ"	: 	Injection Stage 5 speed setting

"RR"	: 	Injection Stage 5 pressure setting

"SS"		: 	Injection overshot detection position setting

"TT"		: 	Injection Holding stage 1 pressure setting

"UU"	: 	Injection Holding stage 1 time setting

"VV"	: 	Injection Holding stage 2 pressure setting

"WW"	: 	Injection Holding stage 2 time setting

"XX"	: 	Injection mode selection: press    to select

one of the following four modes:

(1)	Open loop (standard function)

(2)	Close loop (optional function)

- Open loop + injection hold (optional function)

(4)	Close loop + injection hold (optional function)

Injection time TIM 0

QQ %  RR%   NN %  OO %   KK %  LL %    HH %  II %     EE %  FF %

Inject stage 5   Inject stage 4    Inject stage 3     Inject stage 2     Inject stage 1

↑             ↑             ↑              ↑

Flash          PP mm         MM mm        JJ mm           GGmm

Inject hold stage 2 time    Inject hold stage 1 time

WW sec                UU sec

QQ %   VV %         QQ %   TT %        QQ %   RR %

Inject hold stage 2        Inject hold stage 1       Inject stage 5

3.4.13	Plasticization Setting

Plasticization Setting Screen(14)

PLASTICISING

PLA. TIME	AA	s		CUSHION			BB	mm

DELAY		CC	s		LOW ALARM			DD

SP  	PR		BP				POSIT.

PLAST.1		EE %	FF %	GG %	TO		HH	mm

PLAST.2		II %		JJ %		KK %	TO		LL	mm

DECOMP		MM %	NN %			FOR		OO	mm

MAXIMUM SCREW STROKE					PP	mm

???			????			??? mm			???? mm

(1)	Press  or  to display screen (14)

(2)	Press the cursor key   to select the plasticization parameter settings.

Press the numerical keys to enter the required figures and then press

to complete setting.

Shown on the screen:

"AA"	: 	Plasticizing time Display

"BB"	: 	Injection ending point Display

"CC"	: 	Plasticizing delay time setting (TIM3)

"DD"	: 	Low temp alarm function selection . Use

to set

"EE"		: 	1st stage plasticizing speed setting

"FF"		: 	1st stage plasticizing pressure setting

"GG"	: 	1st stage back pressure setting

"HH"	: 	1st stage plasticizing position setting

"II"		: 	2nd stage plasticizing speed setting

"JJ"		: 	2nd stage plasticizing pressure setting

"KK"	:	2nd stage back pressure setting

"LL"		:	2nd stage plasticizing end position setting

"MM"	:	Decompression speed setting

"NN"	:	Decompression pressure setting

"OO"	:	Decompression stroke setting (0-99mm)

"PP"		:	Maximum screw stroke display

← Decompression stroke →

OO mm

EE %  FF %        II %  JJ %           MM %  NN %

1 stage plasticizing    2 stage plasticizing       Decompression

↑                  ↑                 ↑                      ↑                  BB mm            HH mm              LL mm             LL mm + OO mm

3.4.14	Mould Thickness and Clamping Force Setting

Mould Thickness and Clamping Force Setting Screen(15)

THICK NESS & CLAMPING FORCE

ACT.THICK.			AA	mm

MOLDTHICK.			BB	mm

AUTO ADJUST		CC

FORCE				DD	T			POSITION	EE	p

???bar			????p		??? mm			???? mm

- Press                           to display screen (15)

"AA"	: 	Actual mould thickness display

"BB"	: 	Mould thickness adjust setting

"CC"	: 	Mould clamping force automatic adjustment selection .

Press     to set.

"DD"	: 	Mould clamping force in tons

"EE"		: 	Position for calculation of the mould clamping force in

tons display

- To open the mould to the end position, and close the safety doors.

(3)		Operating procedure for manual mould height adjustment:

Press  the mould will move forward and the mould thickness

will be reduced. If        is pressed, the mould will move

backward and the mould thickness will be increased. To stop the motion just press the key once more.

(4)		For automatic adjustment of mould thickness, operate as follows : (optional function)

First measure the thickness of the mould to be used (say 430.0 mm). Then enter the figure 430.0 to the mould thickness position BB. Now

Press         the mould thickness may be adjusted automatically. If it

is required to stop mould thickness adjustment , press again.

(5)		For automatic adjustment of the mould-locking force, operate as follows : (optional function)

Press   to select this function and enter the mould-locking force in

tons. Then repeat the actions in Step (4). After automatic adjustment of the mould-locking force, the mould-locking force position will be entered directly into the high-pressure start position and thus the function of automatic adjustment of the mould-locking force is completed

3.4.15	Injection Unit Movement Setting

Injection Unit movement Setting Screen (16)

NOZZLE

SP		PR				TIME

NOZ.IN FAST			AA %	BB %			CC	S

NOZ.IN SLOW		DD %	EE % 		TO LIMIT SW

NOZ.OUT			FF %	GG % 		←	HH	S

???bar			????p		??? mm			???? mm

(1)	Press   and   together to display screen (16).

(2)	Press the cursor key  to select the injection unit parameter

settings.

Press the numerical keys to enter the required figures and the press

to complete setting.

Shown on the screen :

"AA"	:	Nozzle in fast speed setting

"BB"	: 	Nozzle in fast pressure setting

"CC"	: 	Nozzle in fast stroke time adjustment (TIM35)

"DD"	: 	Nozzle in slow speed setting

"EE"		: 	Nozzle in slow pressure setting

"FF"		: 	Nozzle out speed setting

"GG"	: 	Nozzle out pressure setting

"HH"	: 	Nozzle out stroke time adjustment (TIM18)

3.4.16	Function Selection Setting

Function Selection Setting Screen (17)

FUNCTIONS

BOOST CLAMP	OF		PHOTO DETECT	OF

AIR BLOW		OF		ROBOT			OF

ACCUM.INJECT	OF		H.INJ ALM		OF

HOLD PRES. SW	TIMER

NOZ.CLOGGED	OF		LEAK.ALARM	OF

VENTING		OF		SEQ CORE		OF

BOOST INJECT	OF		BOOST PLAST	OF

MOLD CHANGE	OF		COLOR CHANGE	OF

HYD.NOZZLE		OF		PRE.DECOMPR	OF

AUTO STOP BY	OFF

???		????		??? mm		???? mm

(1)	Press the key   to show screen (17).

(2)	Press the cursor key   to move the cursor to the function to be

selected.

Press        to select “ON” or press        to select “OFF”.

Press         to complete setting.

- Automatic machine stop option :

Press  or to select one of the following four modes to

suit moulded produce quantity, batch size and breakdown stoppage.

(i)	Stop machine

(ii)	Hydraulic pump power off

(iii)	Heaters power off

(iv)	Hydraulic pump and heaters power off

(4)	Switching of injection holding pressure

(i) by timer :	When timer is selected, the switching of hold pressure is done after the injection time count is up.

(ii) by position switch :	When it is selected, injection holding pressure will start from the injection end position (Inject stage 5 position)

(iii) by pressure switch :	When it is selected, the injection pressure transducer is used, the injection holding pressure will start if the preset injection pressure has been reached.(refer to 3-25) (optional feature)

(5)	Hydraulic nozzle 	 : 	When it is “ON”, the hydraulic nozzle is can be

(optional feature)

(6)	Injection hold alarm : 	When it is “ON” , if the pressure of injection

holding lies outside the presetting range, an alarm message will be given. (optional feature)

The other functions may be understood directly from their verbal meanings and there is no need to describe them here.

3.4.16 + Two times Clamping

The two times clamping function is installed on the “Color Change On/Off” function, which can be seen on the “Function Selection Setting Screen (17)”. Turn “On” the Color Change function, so that the machine runs under the two times clamping mode in semi-automatic or full-automatic mode. 1st clamping motion ends when low-pressure clamping period finishes and then injection carriage forwards and injection starts, 1st injection clamping end position is adjusted by low pressure clamping end position. 2nd clamping and pressure holding will start after injection finishes.

The delay time for 2nd clamping is set on TIM 36, which can be seen on “Timer Monitoring Screen (42)” on page3-80. On SET of TIM 36, you can change from 0.1~0.5.

Note: To prevent the motion impact, the function cannot work together with Boost Clamp. Function two times clamping will be automatically off if function Boost Clamp is on.

3.4.17	Lubrication Setting

Lubrication Setting Screen (18)

LUBRICATION

EVERY		AA	CYC.	LUBE ONECE

LUBE PERIOD:	BB	s

ALARM TIME:	CC	s

REMAINING	DD	CYC. TO LUBE

???		????		??? mm		???? mm

(1)	Press        to show sreen (18).

(2)	Press the cursor key        to select the lubrication parameter

settings.

Press the numerical keys to enter the required figures and then

press        to complete setting.

Shown on the screen,

"AA"   :		Number of moulding between actions of the lubrication,

set in counter CNT 8.

"BB"	: 	Time taken for each lubrication, set in timer TIM 30.

"CC"	: 	Lubrication stroke check time, set in timer TIM31.

(optional feature)

"DD"	: 	Number of moulding before next lubrication.

3.4.18	Counter Setting

Counter Setting Screen(19)

PRODUCTION

SET		ACTUAL

PRODUCTION		AA	t		BB	t

DEFECT				CC	t		DD	t

PRODUCT.TIME		EE	Hr		FF	Hr

BATCH SIZE			GG	t		HH	t

AUX				II	t		JJ	t

AUX				KK	t		LL	t

AUX				MM	t		NN	t

???bar	????p	??? mm		???? mm

(1)	Press   to display screen (19).

(2)	Press the cursor key          to select the completed moulding times

settings.

Press the numeric keys to enter the required figures and then press

to complete setting

Shown on the screen

"AA"	: 	Number of mouldings setting (CNTO)

"BB"	:	Number of moulding times already produced

amongst the set number of mouldings.

"CC"	:	Set number of reject mouldings produced to give out

alarm (CNT 1).

"DD"	: 	The number of reject mouldings already produced

"EE" 	: 	Automatic production time setting (CNT2)

"FF"		: 	Actual production time

"GG"	: 	Batch quantity setting  (CNT3)

"HH" 	: 	The batch quantity already produced

"II"		: 	Auxiliary counter setting (CNT 9)

"JJ"		: 	Current reading of counter

"KK"	: 	Auxiliary counter setting (CNT10)

"LL"	: 	Current reading of counter

"MM"	: 	Auxiliary counter setting (CNT11)

"NN"	: 	Current reading of counter

(3)	For resetting the counter, press the cursor keys  to the current

reading of the counter to be reset, press         and a “?” will be

displayed. To confirm the resetting, press        otherwise press

.

3.4.19	Time Setting

Time Setting Screen (20)

TIME

INJECT		AA		COOLING		BB

HOLD1		CC		RECYCLE		DD

HOLD2		EE		LOW PRES.		FF

PLAST DL	GG		COLOR CH		HH

PRE.DECO	II		EJT DLY			JJ

CYC.ALAR	KK		AIR BLOW1		LL

AUX		MM		AIR BLOW2		NN

???bar	????p	??? mm		???? mm

(1)	Press  to display screen (20).

(2)	Press the cursor key  to select time settings.

Press the numeric keys to enter the required figures and then press

to complete setting.

Shown on the screen:

"AA" 	: 	TIM		0	Injection Stages 1 to end of stage of 5 time

setting.

"BB"	: 	TIM		1	Cooling time setting

"CC"	: 	TIM		9	Injection hold stage 1 time setting

"DD"	: 	TIM 	2 	Recycle time setting

"EE"	: 	TIM 	10 	Injection hold stage 2 time setting

"FF" 	: 	TIM 	6	Low pressure clamping alarm time setting

"GG" 	: 	TIM 	3 	Plasticizing delay time setting

"HH" 	: 	TIM 	32 	Barrel color change time setting (option)

"I I" 		: 	TIM 	4 	Melt decompression before plasticizing

time setting (option)

"JJ" 		: 	TIM		7 	Air blow ejection time setting

"KK"	: 	TIM		5 	Cycle alarm time setting

"LL"	: 	TIM 	8 	Reserve time setting (option)

3.4.20	Timer Setting

Timer Setting Screen (21)

TIMER

Y → Δ			AA		VENT			BB

DECOMP			CC		CLA. DLY		DD

OPEN EJT		EE		EJT. DLY			FF

AIR BLOW		GG		CORE DLY		HH

ALARM T1		II		SCREW DL		JJ

ALARM CY		KK		ACC. DLY		LL

OUTPUT			MM		AUX			NN

???bar	????p	??? mm		???? mm

(1)	Press       and     together for 3 seconds and the screen (21)

will appear.

(2)	Press the cursor key          to select time settings.

Press the numeric keys to enter the required figures and then press

to complete setting.

Shown on the screen,

"AA"	:	TIM 	19 	Motor Y-( start time setting

"BB" 	: 	TIM		25 	Mould open venting time setting

"CC" 	: 	TIM 	36	Mould open pressure release time setting

"DD" 	:	TIM		26 	Mould close delay time setting

"EE" 	: 	TIM 	20 	Reset initial position time setting

"FF" 	: 	TIM 	27	Ejector delay time setting

"GG" 	: 	TIM 	21 	Air blow time setting

"HH" 	: 	TIM 	28 	Core pull delay time setting

"II"		: 	TIM 	22 	Alarm interruption time setting

"JJ"		: 	TIM 	29 	Unscrewing delay time setting

"KK" 	: 	TIM		23 	Alarm cycle time setting

"LL"	:	TIM 	37 	Accumulator injection delay time

"MM"	: 	TIM		24 	limit switch alarm time setting

"NN" 	: 	TIM		38 	Auxiliary timer setting

Note : 	The settings of the timers in this screen have been checked and set in the factory before delivery. They cannot be changed willfully, or else the stability of the machine will be affected.

3.4.21	Adjustment Function Setting

Adjustment Function Setting Screen (22)

SETTING INITIAL VALUE

SPEED REDUCTION

DURING ADJUSTMENT:		AA	%

???bar	????p	??? mm		???? mm

- Press  and  together to display screen (22)

The related LED on the computer panel will light, indicating the "adjustment "function has been activated. The machine speed is then equal to AA% of pre setting value.

For example :	The injection unit and ejector speeds are set at 50%, and the speed limit during adjustment is also 50%.

The machine speed during adjustment is:

50% × 50% = 25%

Note :	The function is designed for "machine adjustment" or "mould adjustment ", it is only effective for manual operation. When the function is activated, the machine can’t be operated in automatic mode. Conversely, when the machine is operated in automatic mode, this function can’t be activated.

Turn off the this function, press and together again.

(2)	"AA" 	: 	Speed limit setting during adjustment operation mode

in %

3.4.22	Mould Number Selection Setting .

Mould Number Selection Screen (23)

| MOLD SELECT |
| --- |
| 001 002 003 004 005 006 | 007 008 009 010 011 012 |
| MOLD POS: MOLD NO: MOLD SEL: | AA BB NAME: DD CC |
| ??? bar | ???? p | ??? mm ???? mm |  |

(1)	Press   to display screen (23).

Shown on the screen,

"AA"	: 	Indicates the location of mould number, press

or           to select the one of the following two modes:

(i)	Computer memory

- Memory card

"BB"	: 	Mould number to be located

"CC"	: 	Mould number in use. In the automatic mode, the mould

number can not be changed, it can be only changed in the

manual mode.

"DD"	: 	Brief description of the mould number.

(2)	How to input the description of the mould number

For example, to change the description of the mould number 01 to "TEST", the procedure is as follows:

- Move the cursor to the position of mould number BB and key in 01.

Press        to complete setting of the mould number.

Press the cursor key to the position of DD and key in

English letters or numerals as codes from the left to right. Enter the

next character by pressing   After the above steps are

completed, press  to complete the setting of the description.

of the mould

number. (By keying in TEST and pressing         the change of

the description of the mould number 01is completed)

- Continuously press the key         to the cyclical display

7(A(B(C-7 will occur. If a blank needs to be keyed in, press the numeric key 3 for successive four times 3(X(Y(Z(blank.

(3)	To change mould from "01" to "02", the procedure is as follows:

(i)	Move the cursor to the mould number selection position CC,

key in 02 and press  .If it is confirmed, press

and if it is not confirmed, press

- There are 1-150 groups of mould number available in the memory. Among them computer-stored mould number 1-99 are standard mould groups. Mould number 100-150 are simple operation mould groups. (For simple operation mould groups, some data can’t be changed, and they can only be changed in the mould number 100).

Since the statement "the mould data could not be changed" means that they could not be copied. Therefore, mould number 100 should not be used freely. Some data of mould number 100 will be supplied to mould number 101-150 the data of which can’t be changed.

3.4.23	Mould Number Copying Setting

Mould Number Copying Screen (24)

MOLD DATA SAVE SCOPY

MOLD﹕		AA			COPY TO MOLD﹕		BB

MOLD﹕		CC	TO	DD		SAVE TO CARD		EE

CARD		FF	TO	GG		COPY TO MOLD		HH

CARD				NAME﹕	II

CARD FORMAT

MOLD SEL﹕	JJ

???bar		????p		??? mm			???? mm

(1)	Press  and  together to display screen (24).

(2)	Only CHEN HSONG memory card can be used. Otherwise the warning messages "Please use Chen Hsong Memory Card" or "Bad Memory card" will appear on the screen, and no copying and writing can be carried out.

(3)	There are two card operating modes : (option)

- For mould number	: 	This is used for storing the mould number

data settings.

(ii)	For statistics 		: 	This is used for storing the moulding

results data.

These two modes are not compatible. If it is wrongly used, warning message will appear on the screen.

(4)	When using the card for the first time or deleting all the content of a card, a format procedure must be carried out as follows:

Select the format of card mode, press  to the "mould data use" or

the "statistics use" position, and then press                  and a warning message

will be displayey on the screen.. Press        to complete the format.

Otherwise, press       to cancel the format.

(5)	To avoid the contents of the card being deleted, the switch on the card may be moved to WP position to protect the integrity of the card content.

(6)	When storing the date in the card without moving the card switch from the "WP" position, the warning message "Please remove the card protection lock" will display on the card.

(7)	If mould number "005 " is to be copied to mould number "010", the procedure is as follows:

Move the cursor to mould number "AA" position, enter 005 and then

press  . Move the cursor to "BB" position, enter 010 and press

again. The question mark"?" appears on the screen. Press

to complete copying.

(8)	If mould number "005-015" are to be copied to cards as "010-020", the procedure is as follows:

Move the cursor to the mould number "CC" position, enter 005 and press

Move the cursor to the "DD" position, enter 015 and press

Then move the cursor to EE position , enter 010 and

press  . Question mark “?” will appear on the screen. Press

to complete copying.

Now the contents of "010-020" on the card are exactly the same as the contents of mould number "005-015" in the computer.

- If "010-020" on the card are to be copied to mould number "005-015", the procedure is as follows :

Move the cursor to the "FF" position, enter 010 and press  . Move

the cursor to "GG" position, enter 020 and press        Move the

cursor to Position"HH",enter 005 and press           Question mark "?"will by

displayed on the screen. Press        to complete copying.

Now the data of mould number "005-015" in the computer are exactly the same as 010-020 on the card.

(10)	"II"	: 	Description of the mould number on the card

(11)	"JJ	: 	Mould number selection display and setting.

3.4.24	Quality Statistics

Quality Statistics Screen (25)

QUALITY STATISTIC

TARGET		CURR.		PREV.		LAST2

CYC.NO.			???			???			???				???

CYC.TI			???			???			???				???

INJ.EN			???			???			???				???

INJ. TI			???			???			???				???

PLA.TI			???			???			???				???

QUALIT						OK			OK				OK

RESET												DEFECT

PRODUC			AAt		ACCEPT			BBt			CC%

???bar		????p		??? mm			???? mm

(1)	Press  and  together to display screen ( 25).

- Move the cursor to the "Target ", and press  or to

switch over the setting of the target and the deviation.

(3)	Cycle No				:	Current moulding cycle number display

Cycle time			:	Current moulding cycle time display

Injection end position	:	Current injection end position display

Injection time			:	Current injection time display (up to the

Injection stage 4 end position)

Plasticizing time		:	Current plasticizing time display

(4)	Move the cursor to the "Target", press        Question mark "?" will

be displayed on the screen, press        and the data values of

“Current Time” will be taken as the data of the “Target value”.

(5)	Move the cursor to the "Deviation", the deviation values of the cycle time, injection end position, injection time and plasticizing time may be changed. If the deviation value is exceeded, the warning signal "NG" (No Good) will appear on the picture and if not, “OK” will appear on the screen.

(6)	Move the cursor to "Last 2" position, press or             to

switch over the settings of the "Last 2" and the average value.

(7)	Move the cursor to "Reset", press        and question mark "?"

will appear on the screen, Press  and the data on the screen

may be reset.

(8)	"AA"	: 	Number of moulding already produced

"BB"	: 	Number of "Reject moulding" already produced

"CC"	: 	The "Reject %" calculation

Note :	The above data can be stored in the statistic mode of the memory card.

3.4.25	Injection End Position Graphic Display

Injection End Position Graphic Display Screen (26)

| INJECTION CUSHION |
| --- |
| ↑ +3 POS.mm 0 |  |  |  |  |  |
| ↓ -3 |  |  |  |  |  |
| CYCLE→ -200 -100 0 |
| ??? bar | ???? p | ??? mm | ???? mm |

(1)	Press  and  together to display screen (26).

(2)	The central position 0 is the setting of the end position of injection stage 4 and the actual injection end position which is relative to the end position of injection stage 4 is shown on the screen.

(3)	To clear the graph, use "data reset" function of the "quality statistic" screen.

(4)	This graph may be		(i)	printed by use of the printing function and

(ii)	stored in the memory card

3.4.26	Pressure Switch Setting

Pressure Switch Setting Screen (27)

PRESSURE SWITCHES

CLAMP PRESS.				AA	BAR

HOLD PRESS.					BB	BAR

MAX PRESSURE				CC	BAR

???bar	????p	??? mm		???? mm

(1)	Press  and  together to display screen (27) (option).

(2)	Press the cursor key  to select the pressure parameter settings.

Press the numerical keys to enter the required figures and then press

to complete setting.

Shown on the screen,

"AA"	: 	Clamping pressure setting

"BB"	: 	Injection holding pressure setting

"CC"	: 	Maximum hydraulic pressure setting

#### Note :  This screen has to be used in conjunction with pressure sensor

3.4.27.1		Initial Position Setting

Initial Position Setting Screen (28)

INITIAL DATA

INITIAL POSIT.			AA	mm

MIN THICKNESS			BB	mm

MAX THICKNESS			CC	mm

MAX PRESSURE			DD	BAR

ENCODERS RESET DATA

PRSET1		EE	P		FF	mm		GG	mm

PRSET2		HH	P		II	mm		JJ	mm

???		????		??? mm		???? mm

(1)	Press  and  together for 3 seconds, screen (28) will be

displayed

(2)	The procedure for setting the initial position of “Mould thickness adjustment” is as follows:

If the mould is on the machine, the mould closes until the toggle is straightened, and the mould can’t be accessed. Measure the actual distance between the stationary and moving platens. Move the cursor to

AA position, enter the figure of the actual distance and press the key

Then move the cursor to Position AA again, press  and

the question mark “?” will be shown on the screen. Press         to

complete the setting. Now the current thickness value on mould thickness screen (11) is changed into the actual distance value.

(3)	"BB": 	It displays the setting for minimum mould thickness

(4)	"CC": 	It displays the setting for maximum mould thickness

(5)	"DD": 	It displays the setting for maximum hydraulic pressure

(6)	"EE":   	Mould clamping pre-set position setting

"FF": 	Ejector pre-set position setting

"GG": 	Injection pre-set position setting

(7)	The operating procedure for setting the encoder is as follows:

- Move the cursor to EE position , enter the required position setting.

and press Move the cursor to Position EE again

and press The question mark “?” appears on the screen.

Press  to confirm and complete the setting. Now the actual

position of the mould is changed into the setting of EE.

(ii)	The setting method for the ejector and injection encoder is the same as that for mould clamping.

(8)	"HH"	: 	Mould clamping position reset (set at Preset2)

"II"		: 	Resetting of the position for ejection (set at Preset2)

"JJ"		: 	Resetting of the position for injection (set at Preset 2)

Caution  : The settings in this screen have been checked and set in the factory before delivery. Don’t arbitrarily change the settings to avoid upsetting the machine stability.

3.4.27.2		The Procedure for Resetting of the Initial Position after a Sudden Power Failure of the Computer

The power supply to the computer may be suddenly cut off. During machine operation. When the computer is restarted, a warning message is shown on the screen reminding the operator to reset the initial position.

Before resetting the initial position check the setting as following:

(i)	On auxiliary Speed and Pressure screen (28), the settings of the speed and pressure for the origin are:

R229 : speed = 50 %,  pressure = 50 %

(ii)	Origin reset timer TIM 20 = 4 sec.

(iii)	Initial position setting screen (25):

Mould Preset 1 position EE = 1 p

Ejector Preset 1 position FF = 0.5 mm

Injection Preset 1 position GG = 0.5 mm

(1)	Clamping

If the power supply to the computer is suddenly cut off during mould clamping or mould opening, the warning message "Reset origin clamp until no alarm " is shown on the screen when the computer is switched on. The method of resetting the initial position for mould clamping is as follows:

- Press  after an interval of 4 seconds on the setting of timer

TIM20 and the toggle are straightened, and the clamping position is automatically changed into mould clamping presetting1 Position EE setting 1p. The warning message disappears and the origin resetting is completed.

OR

- Press  and  together. After an interval of 4 seconds

setting of timer TIM20, and the toggle is straightened the actual clamping position is automatically changed into mould claming preset 1 position (1p), the warning signal disappears and the initial position resetting is completed.

After 4 seconds , if the toggle fail to straight fully, perform the mould-clamp initial position reset again【method (ii)】.

If there are products in the mould, the products must first be ejected out. For detailed operating method, refer to the description of the following pages.

If there are products in the mould, the products must first be ejected out.

The operation is as follows:

- Open the mould till the moving platen stops. At the Mould-clamping Preset 1 position in Initial Position Picture (28), set EE to 9999p the corresponding figure of which shall be greater than the setting value of slow open position (end) position〔Mould-Opening screen (06)〕.

Press   to move the cursor back to the Mould clamping

Preset 1 position and press         The question mark “?” appears

on the screen, press and the actual clamping position is

automatically changed into clamping Preset 1 position 9999p and the warning message disappears.

(ii)	Press       until the signal “Open Ends” is shown on the screen.

(iii)	Press        to eject out the products.

(iv)	Press         to move the cursor back to the clamping preset 1

position and change Item EE from 9999p to 1p.

(v)	Refer to Para.(3) “Method of Manually Adjusting Mould Initial Position” of 3.2.28.3 “Setting Method of the Initial Position of the encoder” of this Operating Manual and readjust the clamping initial position.

(2)	Ejector

If the power supply to the computer is suddenly cut off during ejector movement, the warning message "Reset origin eject until no alarm" is shown on the screen, after the computer is switched on again.

The method of resetting the ejector initial position is as follows :

Press        after expiration of 4 an interval seconds has elapsed of

timer TIM20, the ejector retracts to its end position and the alarm message disappears. Now the actual position of ejection is automatically changed into ejector preset 1 position 0.5mm, and the origin setting is completed.

If the ejector hasn’t retreat to its end position after 4 seconds, carry out ejector origin preset again.

(3)	Injection

If the power supply to the computer is suddenly cut off during injection or plasticization, the warning message "Reset origin injection until no alarm" is shown on the screen after the computer is switched on again.

The method of resetting injection initial position is as follows:

Press  after an interval of 4 seconds has elapsed on the setting of

timer TIM20, injection operation is carried out to its endposition. Then the actual injection position is automatically changed to injection preset 1 position setting 0.5mm and the warning massage disappears and the initial position setting is completed.

If the injection hasn’t been carried out to its final ending position, after an interval of 4 seconds has elapsed on timer TIM20, perform the injection initial point resetting once more.

3.2.27.3		Description on the Encoder Initial Position Setting Screen

- On screen (28), there are clamping preset 1, preset 2, Injection preset 1 Preset 2 and ejector preset 1, preset 2.

- The functions of preset 1 are to change the current value of the encoder position and manually set the initial position.

- The function of preset 2 is to reset the encoder positions.

(2)	The operating method of preset 1

(the method of changing the encoder’s actual position) (clamping).

Move the cursor to EE position of the clamping preset 1, key in the position

setting and press Move the cursor back to the EE position of

preset 1 and press  The question mark “?” is shown on the screen

Press  to complete setting.

Now the current clamping position is the same as the GG position of the clamping preset 1.

(The operating method of Injection Preset 1 and Eject Preset 1 is the same as that of clamping Preset 1 described above).

##### Preset 1 ------- This is for manually setting the initial position

During the machine operation, if the initial position changes, the initial position can be reset by means of manually setting the origin.

(3) 	Method for manually setting the clamping initial position

Before manually resetting the clamping initial position, check the settings as follows:

(i)	The settings of speed and pressure for the origin (screen 31)

R229  speed = 50 % , pressure = 99 %

(ii)	Reset origin time: TIM20 = 4 sec

- Check clamp preset 1 position EE = 1 p

Notes:  (i)	There should be no product in the mould. In case there is, the product must be taken out first.

(ii)	If the mould is equipped with the core-pulling and core-rotating devices. Check their positions and strokes and ensure that the core-pulling and rotating devices are in a safe position to avoid any damage.

Method:	Press  and  simultaneously to

move the toggle forward. After an interval of 4 seconds has expired on the setting of TIM20, the toggle fully extends, and the actual clamping position is automatically changed into EE position 1p of clamping preset 1. The manual setting of the initial position is completed.

If the toggle fails to extend fully, manual setting of the initial position shall be carried out again.

(4)	Method for manually setting the injection initial position

Caution: The temperature of the barrel must reach the setting point

Injection preset 1 position GG = 0.5 mm

Press  to carry out injection till the end position , then press

together at same time. The actual position for injection is automatically changed into the GG position 0.5mm of injection preset 1. The manual setting the injection initial position is completed.

- (5)	Method for manually setting the ejector initial position

Caution: Opening position must be at the end position

Ejector preset 1 FF = 0.5 mm

Press        and the ejector retreats to the end position. Press

together at same time and the actual position for the ejector is automatically changed to the EE position 0.5mm of ejector preset 1.

The function of preset 2 is to reset the encoder position automatically. Preset 2 position is the position of the proximity switch for resetting the origin sensor. The setting of the origin shall be performed on the basis of the position of that proximity switch.

(6) 	Method for setting of clamping preset 2 position

Clamping preset 2 position for the clamping reset sensor. During the mould opening, when the resetting sensor is actuated, the clamping position origin is reset automatically.

(i)		Adjust the mould thickness to ensure the mould parts mounted on the stationary platen and moving platen can not touch each other when the toggle is extend fully. If there is no mould on the platens this step can be ignored.

(ii) 	On the initial position screen (28), enter a greater figure (say, 2000 p) than the position HH p of clamping preset 2.

(iii) 	Change the position of the high-pressure clamp II p to 00 p in the mould clamping screen(05).

(iv)	Carry out clamping and opening operations 3 times in manual mode. Each time when clamping is carried out, the toggle must be fully extended. Each time when opening is performed, IN 32 must be "ON" on I/O monitoring screen(36) while the sensor for resetting the initial position is actuated.

(v) 		After performing the mould clamping operation for 3 times, write down the actual position of the clamp (say 1250 p) when the toggle is fully extended.

(vi) 		The new clamp preset 2 position (the position where the reset sensor is actuated) HH = 2000 p -1250 p = 750 p.

(vii) 		Enter the new value 750 p into the EE position of clamp preset 2.

(viii)		Carry out 3 further clamping and opening operations. If each time the actual clamp end position is below 10 P, the setting clamping preset 2 position (the position of the clamp reset sensor) is completed. If it is a two-digit number or above, repeat steps (Lower case- V-Viii).

- Enter 100p into the position of high-pressure mould clamping in the clamping screen (05).

(7) 	Method for setting the injection preset 2 position

The injection preset 2 position is the position of the injection reset sensor. During plasticization, when the reset sensor is actuated, the injection initial position will be reset automatically.

###### Caution : The temperature of the barrel must reach the set point

(i) 	Enter a comparatively large figure (say 100mm) into the injection preset 2 position JJ p in the initial position screen (28). The figure must be smaller than the setting of plasticization position.

(ii) 	Carry out injection and plasticization operations 3 times in manual mode. Each time when injection is carried out the stroke must be completed until the end position is reached, and only then plasticization started. During plasticization, when the resetting sensor is actuated, IN 33 must be "ON" on the I/O monitoring screen (36).

(iii) 	After performing the injection operation for 3 times and when the injection stroke comes to its end position, record the actual position of injection (for example, 68mm).

(iv) 	The new injection preset 2 position (the position where the resetting sensor is actuated) JJ = 100 mm-68 mm = 32 mm.

(v) 	Enter the new figure 32mm into the JJ position of injection preset 2.

(vi) 	Carry out 3 further injection and plasticization operations. If the actual end position of the injection stroke is below 0.5mm, the setting of injection presetting 2 position (the position of injection resetting sensor) is completed. If such end position is above 0.5mm.

Steps (iii)- (vi) shall be repeated.

(8) 	Method of setting of ejector preset 2 position:

The ejector preset 2 position is for the ejector reset sensor. When the ejector backward is completed and the reset sensor is actuated, the initial position will be reset automatically.

Caution : The mould-opening stroke must reach its end position.

(i) 	Enter a comparatively larger figure (say 15mm) into the ejector preset 2 position II p in initial position setting screen (28).

(ii)	Carry out ejector forward and backward operations 3 times for each in manual mode. The ejector backward must be carried out to its end position each time. When the injection resetting sensor is actuated, IN34 must be "ON" on the I/O monitoring screen (36).

(iii) 	After performing the ejector forward and backward operations 3 times and the ejector backward has been carried out to the end position, record the actual position of ejector (for example, 8.5mm).

(iv) 	The new ejector presetting 2 position (the position where the resetting sensor is actuated) II = 15 mm - 8.5 mm = 6.5 mm.

(v) 	Enter the new figure 6.5mm into Item II of injection preset 2 position.

(vi) 	Carry out 3 further ejector forward and backward operations. If each time the ejector backward end position is below 1mm, the setting of ejection presetting 2 position (the position of ejector resetting sensor) is completed. If such an end position is above 1mm, Steps (iii)-(vi) shall be repeated.

Caution :	The settings on this screen have been tested before delivery of the machine. If it is not necessary, do not try to change the settings willfully so as to avoid the possibility of impairing the stability of the machine.

3.4.28	Ramp Up/Down Setting

Ramp Up/Down Setting Screen (29)

RAMP SETTINGS

SP					PR				BP

R304	AA %		R309	BB %	R314	CC %

R305	DD %		R310	EE %	R315	FF %

R306	GG %		R311	HH %	R316	II %

R307	JJ %		R312	KK %	R317	LL %

R308	MM %		R313	NN %	R318	OO %

CONSULT CHEN HSONG WHEN CHANGED.

???bar		????p		??? mm		???? mm

(1)	Press and together for 3 seconds, Screen (29)

will appear.

(2) 	Press the cursor key   to select the items for setting. Press the

numeric keys to enter the required figures. Then press  to

complete setting.

Shown on the screen:

"AA"	: 	Speed ramp1 proportional setting (The greater the

setting, shorter the ramp time) (For mould clamping)

"BB"	: 	Pressure ramp1 proportional setting (The greater the

setting, the shorter the ramp time). (for mould-locking)

"CC"	: 	Back pressure ramp 1 proportional setting (The greater the

setting, the shorter the ramp time) (for mould-opening)

"DD"	: 	Speed ramp 2 proportional setting (The greater the

setting, the shorter the ramp time) (for mould-opening)

"EE"	: 	Pressure ramp 2 proportional setting (The greater the

setting, the shorter the ramp time) (for mould-opening)

"FF"		: 	Back pressure ramp 2 proportional setting (The greater the

setting, the shorter the ramp time) (for mould-opening)

"GG"	: 	Speed ramp 3 proportional setting (The greater the

setting, the shorter the ramp time)

"HH”	: 	Pressure ramp 3 proportional setting (The greater the

setting, the shorter the ramp time)

"II"		: 	Back pressure 3 proportional setting (The greater the

setting, the shorter the ramp time) (for mould-opening)

"JJ"		: 	Speed ramp 4 proportional setting (The greater the

setting, the shorter the ramp time)

"KK"	: 	Pressure ramp 4 proportional setting (The greater the

setting, the shorter the ramp time)

"LL"		: 	Back pressure ramp 4 proportional setting (The greater the

setting, the shorter the ramp time) (for mould-opening)

"MM"	: 	Speed ramp 5 proportional setting (The greater the

setting, the shorter the ramp time)

"NN"	: 	of Pressure ramp 5 proportion setting (The greater the

setting, the shorter the ramp time)

"OO"	: 	Back pressure ramp 5 proportional setting (The greater the

setting, the shorter the ramp time) (for mould-opening)

Caution :  The settings on this screen have been tested before delivery of the machine. If it is not necessary, do not try to change the settings willfully, or else the stability of the machine may be impaired.

3.4.29.1    Auxiliary Speed and Pressure Setting

Auxiliary Speed and Pressure Setting Screen(30)

PRESS/SPEED

SP		PR

NOZZLE			R221			AA %	BB %

CHARGING		R222			CC %	DD %

LOCKING		R223			EE %	FF %

HALF NUT		R224			GG %	HH %

S.LPC			R225			II %		JJ %

UNSCREW3		R226			KK %	LL %

CONSULT CHEN HSONG WHEN CHANGED

???bar		????p		??? mm		???? mm

(1)	Press  and  together for 3 seconds, screen (30 )

will be shown.

(2)	Press the cursor key  to select the appropriate items. Press the

numeric keys to enter the required figures and then press to

complete setting.

Shown on the screen:

"AA"	: 	Hydraulic nozzle speed setting .

"BB"	: 	Hydraulic nozzle pressure setting

"CC"	: 	Accumulator charging speed setting

"DD"	: 	Accumulator charging pressure setting

"EE"		: 	Hydraulic mould fixing speed setting

"FF"		: 	Hydraulic mould fixing pressure setting

"GG"	: 	Hydraulic rotary gate speed setting

"HH"	: 	Hydraulic rotary gate pressure setting

"II"		: 	Special low pressure speed setting

"JJ"		: 	Special low pressure setting

"KK"	: 	Unscrew 3 speed setting

"LL"		: 	Unscrew 3 pressure setting

Caution :  The settings of speed and pressure in this picture have been tested before delivery of the machine. If it is not necessary, do not try to change the setting willfully, or else the stability of the machine may be impaired.

3.4.29.2		Auxiliary Speed and Pressure Setting

Auxiliary Speed and Pressure Setting Screen (31)

PRESS / SPEED

SP		PR

MOLD ADJ→		R227			AA %	BB %

MOLD ADJ←		R228			CC %	DD %

ORGIN			R229			EE %	FF %

FORCE			R217			GG %	HH %

AUX			R230			II %		JJ %

AUX			R231			KK %	LL %

CONSULT CHEN HSONG WHEN CHANGED.

???bar		????p		??? mm		???? mm

- When screen (31) is shown, use the cursor keys  to switch between the screens (30), (31) and (32).

- Press  to select the appropriate items, press the numeric keys to

enter the required figures and then press  to complete setting.

Shown on the screen:

"AA"	: 	Hydraulic mould adjust forward speed setting

"BB"	: 	Hydraulic mould adjust forward pressure setting

"CC"	: 	Hydraulic mould adjust backward speed setting

"DD"	: 	Hydraulic mould adjust backward pressure setting

"EE"		: 	Initial position reset speed setting

"FF"		: 	Initial position reset pressure setting

"GG"	: 	Low pressure automatic mould clamping force adjustment

speed setting

"HH"	: 	Low pressure automatic mould clamping force adjustment

pressure setting

"II"		: 	Reserved function 1 speed setting .

"JJ"		: 	Reserved function 1 pressure setting

"KK"	: 	Reserved function 2 speed setting

"LL"		: 	Reserved function 2 pressure setting

Caution : The settings on this screen have been tested before delivery of the machine. If it is not necessary, do not try to change them willfully, or else the stability of the machine will be impaired.

3.4.29.3    Auxiliary Speed and Pressure Setting

Auxiliary Speed and Pressure Setting Screen (32)

PRESS / SPEED

SP		PR

DECOMPRES.		R233		AA %	BB %

OPENNING		R234		CC %	DD %

H.P.LOCK		R235		EE %	FF %

L.P.LOCK		R236		GG %	HH %

AUX			R232		II %		JJ %

EJT.IN			R206		KK %	LL %

OPEN AUX 2					TO		MM P

CONSULT CHEN HSONG WHEN CHANGED.

???bar		????p		??? mm		???? mm

(1) 	After screen (32) is shown, use the cursor key to switch between the screen(30), (31), (32)

(2) 	Press the cursor key        to select the appropriate setting

items. Press the numeric keys to enter the required figures and then

press  to complete setting.

Shown on the screen:

"AA"	: 	Big cylinder pressure release speed setting .

"BB"	: 	Big cylinder pressure release pressure setting.

"CC"	: 	Big cylinder mould opening speed setting.

"DD"	: 	Big cylinder mould opening pressure setting.

"EE"		: 	Big cylinder high-pressure speed setting.

"FF"		: 	Big cylinder high-pressure pressure setting.

"GG"	: 	Big cylinder low pressure speed setting.

"HH"	: 	Big cylinder low pressure setting.

"II"		: 	Reserved function 3 speed setting.

"JJ"		: 	Reserved function 3 pressure setting.

"KK"	: 	Ejector backward 2 speed setting .

"LL"		: 	Ejector backward 2 pressure setting.

"MM"	:	Mouuld open reserved function (2) end position setting

Caution :  The settings of speed and pressure have been tested before delivery of the machine. If it is not necessary, do not try to change them willfully, or else the stability of the machine will be impaired.

3.4.30    Ladder Program Monitoring

Ladder Program Monitoring Screen (33)

CIRCUIT MONITOR

ST.		SET		ACTUAL

0000		LD		1234	0

0001		AND	2345	0

0002		OR		3456	0

0003		ORI		4567	0

0004		ANI		5678	0

0005		OUT		9999	0

0006		TIM		T10			0		6.5			6.5

0007		CNT		C11			0		5.5			5.5

OUT		AA		TIM		BB		CNT		CC

???bar		????p		??? mm			???? mm

(1)	Press  and  together to show screen (33).

(2)	"AA"	:	The position for entering the internal relay number and locate its output. When the internal relay number is entered, the location of its output in the program will be shown.

"BB"	:	The position for entering the internal timer number and locate its output. When the internal timer number is entered, the location of its output in the program will be shown.

"CC"	:	The position for entering the internal counter number and to locate its output. When the internal counter number is entered, the location of its output in the program will be shown.

OUT(TIM(CNT 	These items may be switched between

them by using the cursor key

(3) 	Example	 : 	To locate the output of relay 710 in the program, move the  cursor to the input position of the relay output, enter the 710, the location of the output of relay 710 in the program will be shown.

(4) 	The operating method for the timer and counter is the same as that for the relay.

3.4.31    Input / Output Monitoring

- Press  and  simultaneously to show screen (34).

Input /Output Monitoring Screen(34)

I / O MONITOR	0﹕ON	0﹕OFF

I00	FRONT DR	0		I08	CORE IN		0

I01	REAR DR	0		I09	CORE OUT	0

I02	SAFE DR		0		I10	PHOTOEYE	0

I03	NOZ FOR	0		I11	ACC END	0

I04	CORE 2 -		0		I12	RB.INT		0

I05	CORE 2 +	0		I13	EJT INT		0

I06	SCREW -		0		I14	CYCLE S		0

I07	SCREW +	0		I15	SCREW S	0

???bar		????p		??? mm		???? mm

- When screen (34) is shown, use the cursor keys to switch

between screens (34), (35), (36), (37), (38), (39).

Input / Output Monitor Screen (35)

I / O MONITOR	0﹕ON	0﹕OFF

I16	MD AJ OL	0		I24	GATE IN		0

I17	PUMP OL	0		I25	GATE OUT	0

I18	MD ADJ -	0		I26	LP CLAMP	0

I19	MD ADJ +	0		I27	HP CLAMP	0

I20	MD ADJ S	0		I28	CLA END	0

I21	LUB LV		0		I29	PRE REL		0

I22	LUB PRE		0		I30	CLA LMT	0

I23	LP.C DET	0		I31	OPEN LMT	0

???bar		????p		??? mm			???? mm

Input / Output Monitoring Screen (36)

I / O MONITOR	0﹕ON	0﹕OFF

I32	CLA SET		0		I40	NOZ GUD	0

I33	INJ SET		0		I41	CLAMPER	0

I34	EJT SET		0		I42	OIL TEMP	0

I35	DR OPEN	0		I43	OILDRAIN	0

I36	DR CLOSE	0		I44	HEATER		0

I37	FILTER		0		I45	MD CHANG	0

I38	AUX		0		I46	AUX		0

I39	AUX		0		I47	AUX		0

???			????			??? mm			???? mm

Input / Output Monitoring Screen (37)

I / O MONITOR	0﹕ON	0﹕OFF

O00	 MD ADJ -	0		O08	 MD OPEN	0

O01	 MD ADJ +	0		O09	 EJT FOR		0

O02	 CLAMP		0		O10	 EJT BACK	0

O03	 NOZ FOR	0		O11	 BOOST		0

O04	 INJECT		0		O12	 CORE IN	0

O05	 PLAST		0		O13	 CORE OUT	0

O06	 MELTDEC	0		O14	 SCREW -	0

O07	 NOZ BACK	0		O15	 SCREW +	0

???			????			??? mm			???? mm

Input / Output Monitoring Screen (38)

I / O MONITOR	0﹕ON	0﹕OFF

O16	 ACC CHG	0		O24	 DR OPEN	0

O17	 ACC REL	0		O25	 DR CLOSE	0

O18	 AIR			0		O26	 AUX PUMP	0

O19	 PRE REL	0		O27	 AUTO INJ	0

O20	 GATE IN		0		O28	 OPEN END	0

O21	 GATE OUT	0		O29	 DOOR INT	0

O22	 HP CLA		0		O30	 BACK PRE	0

O23	 HP OPEN	0		O31	 CORE 2		0

???bar		????p		??? mm			???? mm

Input / Output Monitoring Screen(39)

I / O MONITOR	0﹕ON	0﹕OFF

O32	 CORE 2 +	0		O40  AUX			0

O33	 AUX		0		O41  AUX			0

O34	 AUX		0		O42  AUX			0

O35	 AUX		0		O43  MT RUN		0

O36	 AUX		0		O44  LUB			0

O37	 AUX		0		O45  ALARM			0

O38	 AUX		0		O46  DRAIN			0

O39	 AUX		0		O47  PUMP ST		0

???bar		????p		??? mm			???? mm

3.4.32		Input / Output Status Monitoring Screen

Input / Output status monitoring Screen (40)

RELAY MONITOR

0123456789				0123456789

0000	0000000000		0130	0000000000

0010	0000000000		0140	00000000

0020	0000000000		0200	0000000000

0030	0000000000		0210	0000000000

0040	0000000000		0220	0000000000

0100	0000000000		0230	0000000000

0110	0000000000		0240	0000000000

0120	0000000000		0250	0000000000

0=OFF			0=ON

???bar		????p	??? mm			???? mm

- Press  and  simultaneously to show Screen (40).

In this screen, the operating status of all the relays may be checked.

(2)	If any relays other than those covered in this screen need to be checked,

switching over will occur by using the cursor key

Input / Output status monitoring Screen (41)

RELAY MONITOR

0123456789				0123456789

0260	0000000000		0340	0000000000

0270	0000000000		0350	00000000

0280	0000000000		0400	0000000000

0290	0000000000		0410	0000000000

0300	0000000000		0420	0000000000

0310	0000000000		0430	0000000000

0320	0000000000		0440	0000000000

0330	0000000000		0450	0000000000

0=OFF			0=ON

???bar		????p		??? mm			???? mm

3.4.33		Timer Monitoring Screen

Timer Monitoring Screen (42)

TIMER MONITOR

TIM		SET		ACTUAL		TIM		SET		ACTUAL

00		50			50		08		5			5

01		100			100		09		10			10

02		5			5		10		10			10

03		5			5		11		5			5

04		1			1		12		20			20

05		300			300		13		20			20

06		30			30		14		20			20

07		30			30		15		20			20

???bar		????p		??? mm			???? mm

- Press  and  simultaneously for 3 seconds to show screen

(42).

- In this screen , the operating status of all the timers may be monitored. If the timers other than those covered in this screen need to be checked,

screen switching will ocour by pressing the cursor key

(3)	If it is required to change the setting of a timer, move the cursor by

pressing the cursor key  to the position of the setting of the timer

requiring change, enter the desired figure and then press the key

to complete the setting.

Timer Monitoring Screen (43)

TIMER MONITOR

TIM		SET		ACTUAL		TIM		SET		ACTUAL

16		10			0		24		50			0

17		10			0		25		0.1			0

18		10			0		26		0.1			0

19		30			30		27		0.1			0

20		0.1			0		28		0.1			0

21		0.1			0		29		0.6			0

22		100			0		30		30			0

23		100			0		31		40			0

???bar		????p		??? mm			???? mm

TIMER MONITOR

TIM		SET		ACTUAL		TIM		SET		ACTUAL

32		10			0		 40		0			0

33		10			0		 41		0			0

34		10			0		 42		0			0

35		30			30		 43		0			0

36		0.1			0		 44		0			0

37		0.1			0		 45		0			0

38		100			0		 46		0			0

39		100			0		 47		0			0

???bar		????p		??? mm			???? mm

TIMER MONITOR

TIM		SET		ACTUAL		TIM		SET		ACTUAL

48		1.0			0

49		1.0			0

???bar		????p		??? mm			???? mm

3.4.34		Counter Monitoring Screen

Counter Monitor Screen (44)

COUNTOR MONITOR

CNT		SET		ACTUAL		CNT		SET		ACTUAL

00		5000		1000			08		10		5

01		1000		100			09		0		0

02		100		50			10		0		0

03		100		0			11		0		0

04		2		0			12		0		0

05		2		2			13		0		0

06		20		0			14		0		0

07		20		0			15		15		0

???bar		????p		??? mm			???? mm

COUNTOR MONITOR

CNT		SET		ACTUAL		CNT		SET		ACTUAL

16		5000		1000

17		1000		100

18		100		50

19		100		0

???bar		????p		??? mm			???? mm

(1) 	Press  and  simultaneously to show Screen (44).

(2) 	On this screen, the operating status of all the counters may be checked.

- If it is required to change the settings of a counter, move the cursor by

pressing the cursor key   to the position of the counter setting

requiring change, enter the required figure and then press the key

to complete the setting.

3.4.35		Language Selection and Memory Erase

Language Selection Screen (45)

中國語 / 英語 / 日本語選擇

AA	中國語	(Chinese Character)

BB	英語		(English Character)

CC	日本語	(Japanese Character)

記憶資料初期化	(RAM DATA INITIAL)

DD

(1) 	Press  and   simultaneously and switch on the power

supply to the computer until Screen (45) is shown.

- To change the display language, proceed as follows:

If it is required to use English titles for the display, move the cursor to the

Position "AA", press  and all the operating screens will be

displayed with English titles. If it is desired to use Chinese titles for the display, move the cursor to the Position "BB" and Press the key INPUT. Then all the operating pictures will be displayed with Chinese titles.

(3)	If all the memory data need to be erased, move the cursor to the Position

"CC", enter the corresponding confidential codes and press        and

then the question mark “?” will be shown on the screen. If the operation

is to be confirmed, press         to complete the operation for erasing

all memory data. If the operation is to be cancelled, press         to

cancel the operation.

Note : Memory erase means clearing off all data from all memories. The operator is requested to confirm such an operation carefully before Carrying out this operation.

3.4.36	Speed Linearization

Speed Linearization Adjustmen Screen (46)

SPEED LINEARIZE

調整速度 ﹕	0 %			基準DATA ﹕0rpm

出力DATA ﹕00H			現在DATA ﹕0rpm

0 %		0 %		0 %		0 %		0 %

00H		00H		00H		00H		00H

0		0		0		0		0

0 %		0 %		0 %		0 %		0 %

00H		00H		00H		00H		00H

0		0		0		0		0

PUSH ENTER KEY

- Press  and  simultaneously and switch on the power supply

to the computer until screen (46) is shown.

- Press  the speed linearization is then carried out automatically by the

machine with the assistance of the computer. At the same time, the values of all linearization points are shown on the screen.

(3) 	When “LINEA-RIZE START” is shown on the screen, it means speed linearization hasn’t been completed yet. Only when “LINEARIZE END” is shown, the operation of speed linearization has been ended.

(4) 	This Screen is a option.

3.3.37	Pressure Linearization

Pressure Linearization Screen (47)

PRESSURE LINEARIZE

調整壓力 ﹕	0 %			基準DATA ﹕0bar

出力DATA ﹕00H			現在DATA ﹕0bar

0 %		0 %		0 %		0 %		0 %

00H		00H		00H		00H		00H

0		0		0		0		0

0 %		0 %		0 %		0 %		0 %

00H		00H		00H		00H		00H

0		0		0		0		0

PUSH ENTER KEY

(1) 	Press   and  simultaneously and switch on the power

supply to the computer until Screen (47) is shown.

(2) 	Press  and pressure linearization is now carried out automatically

- by the machine with the assistance from the computer and the values of all the linearization points are automatically shown in the screen.

(3) 	When “LINEARIZE START” is shown on the screen, it means that pressure linearization hasn’t been completed yet. Only when “LINEARISE END” is shown, the operation of pressure linearization is completed.

(4)	This Screen is an option.

3.4.38	Speed and Pressure Adjustment

Speed and Pressure Adjusting Screen (48)

速度 / 壓力 				調整

速度						速度

**%		**%		**%		 **%

0	KEY ---	0%			1	KEY ---	10%

2	KEY ---	20%			3	KEY ---	30%

4	KEY ---	40%			5	KEY ---	50%

6	KEY ---	60%			7	KEY ---	70%

8	KEY ---	80%			9	KEY ---	90%

•	KEY ---	99%

- Press  and  simultaneously and switch on the power supply

to the computer until Screen (48) is shown.

(2)	Without starting the oil pump, when the key 0,2,4,6 or 8 is pressed, the current provided by the computer to the proportional flow valve is 200mA, 296mA, 392mA, 488mA, 584mA or 680mA respectively. Similarly when the key 1,3,5,7 or 9 is pressed, the current provided by the computer to the proportional pressure valve is 260mA, 380mA, 500mA, 620mA or 740mA respectively.

(3) 	When any of the numeric keys or the full-stop key. is pressed, the corresponding speed or pressure in percentage will be shown on the screen.

(4) 	By making use of this function the current output linearity of speed and pressure may be easily checked and adjusted.

Note : The current values of flow and pressure proportional valves may be measured with the current meter (ammeter) in the electric control box.

3.4.39	Air Blow Setting

AIR BLOW

AIR 1 START AT OPEN POS.					AA	mm

AIR 1 BLOW TIME							BB	s

AIR 2 START AT OPEN END POS.

AIR 2 BLOW TIME							CC	s

???bar		????p		??? mm		???? mm

Air BlowSetting Screen (49)

- Press  two times to display Screen (49)。

- Move the cursor ，select air blow 1 setting for various stages. Key in numerical data, then press  to complete the setting.

Shown on the screen:

“AA”:	air blow 1 start at open positon setting.

“BB”:	air blow 1 time.

“CC”:	air blow 2 time.

3.5   Alarm Message and Trouble Shooting

3.5.1  Description of Computer Warning Message

| Relay No. | Alarm Message | Description |
| --- | --- | --- |
| 700 | Alarm 1 | Not used |
| 701 | Alarm 2 | Not used |
| 702 | Barrel temperature not reach | The actual temperature in the barrel pipe is lower than the setting temperature for the barrel minus the deviation |
| 703 | Lubrication oil not reach | The oil level of the storage tank of lubrication oil is too low (INPUT 21) |
| 704 | Lubrication release valve clog | Not used |
| 705 | Lubrication oil press. Too low | Not used |
| 706 | Pump motor overload | Check the oil pump motor overload (IN16) |
| 707 | Mould adjust motor overload | Check the mould-adjust motor overload (IN17) |
| 708 | Rear door not close | Close the rear safety door and check the limit switch for the same (IN1) and (IN23 for CE) |
| 709 | Front door not close | Close the front safety door and check the limit switches for the same (IN0&2) |
| 710 | Mould adjustment minimum. limit | The mould thickness is less than the minimum thickness or check the front limit switch for mould-adjusting (INPUT 18) |
| 711 | Mould adjustment maximum. limit | The mould thickness exceeds the maximum thickness or check the front limit switch for mould-adjusting (IN 19) |
| 712 | Alarm 3 | Not used |
| 713 | Pump motor not start | Not used |
| 714 | Clamp end | It shows that mould clamping action has ended during manual operation |
| 715 | Open end | It shows that mould-opening action has ended during manual operation |
| 716 | Open not end | It shows that mould-opening stroke has not ended during manual mould-adjusting or ejector operation |
| 717 | Ejector for end | It shows during manual operation that the ejection operation is ended |
| 718 | Ejector back end | It shows during manual operation that the ejector- back operation is ended |
| 719 | Plast end | It shows during manual operation that the plasticization operation is ended. |
| 720 | Screw back end | It shows during manual operation that the melt decompression operation is ended. |
| 721 | Check nozzle for Limit | The limit switch for carriage forward has not been triggered during automatic operation (IN 3) |
| 722 | Nozzle guard not close | The purge guard fails to be closed during injection (IN40) |
| 723 | Nozzle block | When the “NOZZLE CLOGGED” function is turned “ON” the injection stroke hasn’t reached Injection Zone 2 yet or the nozzle is blocked by foreign matters. Check the injection position setting or nozzle |
| 724 | Short shot or over shot | When the “LEAK ALARM” function is turned “ON” the injection stroke has gone beyond the injection overflowing position. Adjust the injection overflowing position setting or the end position of plasticization. |
| 725 | No material or blocked | During automatic operation, the plasticization time exceeds the cooling time setting. Check for hopper blocking or the being too long setting of the plasticization delay time |
| 726 | Cycle count completed | The actual cycle counter has reached the production counter setting under manual operation condition |
| 727 | Cycle time too long | The production cycle time exceeds the alarm setting of the cyclic time. Check whether the alarm setting of the cyclic time (TIM5) is too short |
| 728 | Please clean up the mould | There are Plastics in the mould or the high-pressure clamp position and the low-pressure time settings are not correct. Check the mould or settings for the high-pressure clamp position and low-pressure time (TIM6) |
| 729 | Mould-adjust too long | Not used |
| 730 | Lubrication in progress | Displayed during lubrication oil pump working |
| 731 | Please check robot fixture | Not used |
| 732 | Take out failure | Not used |
| 733 | Photo cut alarm | When the “photo cell” is used for recycle, the photo cell sensor is covered. Please clean off the products or foreign matters on the slide way. |
| 734 | Power off then on again | Not used |
| 735 | Oil filter clog | Not used |
| 736 | Oil temp too low | The actual temp of the hydraulic oil is lower than the setting for the same (-allowed deviation) |
| 737 | Oil temp too high | The actual temp of the hydraulic oil is higher than the setting for the same (+ allowed deviation) |
| 738 | Auto mould-change | Not used |
| 739 | Nut closing not align | Not used |
| 740 | Check core pull limit | During automatic operation the core-pulling time exceeds the setting of the limit alarm time of the core-pulling operation. Check the core-pulling stroke or limit alarm time (TIM24) |
| 741 | Check gate in / out limit | Not used |
| 742 | Check ejector limit | During automatic operation the ejection time exceeds the setting of the limit alarm time of the ejector operation. Check the ejection stroke (IN34) or limit alarming time (TIM24). |
| 743 | Check valve for door | Not used |
| 744 | Big cylinder not Located | Not used |
| 745 | Open pressure release trouble | Not used |
| 746 | Big cylinder over travel | Not used |
| 747 | Clamping in progress | Not used |
| 748 | Acc. charge alarm | When Nitrogen injection is “ON”, charging time exceeds cooling time (TIM01). Please check the charging pressure switch. |
| 749 | Oil level too low | Not used |
| 750 | Mould adjust sensor trouble | During mould-adjustment the mould adjustment sensor is found to be faulty. Please check the mould-adjustment sensor. |
| 751 | Mould adjust gear trouble | Not used |
| 752 | Mould fitting position check | Not used |
| 753 | Hydraulic clamp trouble | Not used |
| 754 | Clamp force for enough | Not used |
| 755 | Air pressure for robot too low | Not used |
| 756 | Back pressure too high | Not used |
| 757 | Material change in progress | Not used |
| 758 | Preheat in progress | Preheat function turn ON |
| 759 | Check unscrew counting sensor | During automatic operation, the ejection time exceeds the setting of the limit alarm time. Check the ejection stroke or limit setting time (TIM24) |
| 760 | Auto mould thick adjust in progress | Not used |
| 761 | Auto mould clamp force adjust in progress | Not used |
| 762 | AMC table L.S. error | Not used |
| 763 | Pressure sensor detect error | Not used |
| 764 | Plast RPM sensor detect error | Not used |
| 765 | Control cabinet door not close | Not used |
| 766 | Change battery | Not used |
| 767 | Auto mould clamp force complete | Not used |
| 768 | Auto mould thick adjust complete | Not used |
| 769 | Injection setting not god | Not used |
| 770 | Barrel temperature too high | The actual temperature of the barrel is higher than the setting of the same plus the allowed deviation |
| 771 | Plasticization delay | Not used |
| 772 | Mould adjust in progress | Not used |
| 773 | Table in rotation | Not used |
| 774 | Stopper not return | Not used |
| 775 | Auto mould adjust error | Not used |
| 776 | Stepper error | Not used |
| 777 | Push power on switch twice | Not used |
| 778 | Ejector plate not return | Not used |
| 779 | Safety valve error | Not used |
| 780 | Clamp/Open mould trouble | During automatic operation the clamping opening time exceeds the limit alarm time. Check the clamping and opening stroke settings or limit time (TIM24) |
| 781 | Door limit switch error | Not used |
| 782 | Door latch error | Not used |
| 783 | Air pressure not enough | Not used |
| 784 | Safety valve error | Not used |
| 785 | Plasticization not done | Not used |
| 786 | Preform not drop | Not used |
| 787 | Mould open end error | Not used |
| 788 | Plasticization in progress | Not used |
| 789 | Robot safety check error | Not used |
| 790 | Robot not zero return | Not used |
| 791 | Robot alarm | During mould clamping and mould opening, the robotic arm hasn’t risen to the right place. Please check the robotic arm. |
| 792 | Servo control alarm | Not used |
| 793 | Product eject out error | Not used |
| 794 | Open end position error | Not used |
| 795 | Safety close check error | Not used |
| 796 | Plasticization not end | Not used |
| 797 | Preform not drop | Not used |
| 798 | Clean up barrel | Not used |
| 799 | Adjustment! | Not used |
| 800 | Gate in not end | Not used |
| 801 | Barrel temperature too low | Not used |
| 802 | Safety door limit error | Not used |
| 803 | Safety door latch error | Not used |
| 804 | Aux. | Aux. |
| 805 | Aux. | Aux. |

3.5.2	Description of Alarm Message of System Faults

| No. | Chinese Title | English Title |
| --- | --- | --- |
| 1 |  | Ladder program error |
| 2 |  | Please change battery |
| 3 |  | Please connect battery |
| 4 |  | Data is lost, initialize data |
| 5 |  | Data is lost, please change battery |
| 6 |  | Data is lose, please connect battery |
| 7 |  | Reset origin clamp until no alarm |
| 8 |  | Reset origin inject until no alarm |
| 9 |  | Reset origin inject backward until no alarm |
| 10 |  | RAM check error |
| 11 |  | Please check thermocouple |
| 12 |  | Adjustment! Manual mode only |
| 13 |  | Key lock mode |
| 14 |  | Not screw key for preheat |
| 15 |  | Auto mold adjustment |
| 16 |  | Enter/Cancel key is not press |
| 17 |  | Mold adjustment can manual only |
| 18 |  | Mold adjustment! Manual only! |

3.5.3	Description of Titles of Faults

| No. | Chinese Title | English Title |
| --- | --- | --- |
| 1 |  | Please enter correct data |
| 2 |  | Data input is too large |
| 3 |  | Manual mode only |
| 4 |  | Not find |
| 5 |  | “Enter” or “Cancel” key only |
| 6 |  | Not “.” Key |
| 7 |  | “+” or “-” key only |
| 8 |  | Auto mold change! Please Wait! |

3.6		Mould Operation Instruction

3.6.1  Temperature Control Setting

When the power is turned on the temperature display appears. Refer to screen (01). When the symbol “◢ ” is shown in the picture, it means that the electric heater is switched on and the temp control key light shines.

(1) 	Settings of temperature for all zones:

For the temperature setting of Zone 1, press  the position of

temperature is set at T1 on the screen and reverse cursor is produced. Then

enter the required figures and press to input the data into the

computer. Now the cursor moves to the setting of the next zone.To stop the temperature setting, press  to clear the cursor.

For the temperature setting of Zone 2, except for pressing  the other steps are the same as for the temperature setting of Zone 1.

For the temperature setting of Zone 3, except for pressing  the other steps are the same as for the temperature setting of Zone 1.

For the temperature setting of Zone 4, except for pressing  the other steps are the same as for the temperature setting of Zone 1.

For the temperature setting of Zone 5, except for pressing  the other steps are the same as for the temperature setting of Zone 1.

For the temperature setting of Zone 6, except for pressing  the other steps are the same as for the temperature setting of Zone 1.

For the temperature setting of Zone 7, except for pressing  the other steps are the same as for the temperature setting of Zone 1.

For the temperature setting of Zone 8, except for pressing  the other steps are the same as for the temperature setting of Zone 1.

Among all the temperature zones, the settings of Zones 5 and 6 are subject to the machine type and requirements of the customer. When the machine is equipped with the oil temperature control device, the control function will be effected via the temperature of Zone 6. The standard value is normally within the range of 35℃-40℃. TC7 relay output from the I/O board controls the opening and closing of the water gate to make the oil temperature consistent with requirements.

Normally the setting of the high-temperature positive deviation of the temperature of Zone 6 is 15℃, and low-temperature negation deviation is 30℃. Thus when the setting of the standard oil temperature is 35℃, its allowable range will be 5℃-50℃. When the oil temperature goes beyond this range, an alarm will be given.

- Setting of the temperature of the nozzle zone.

The temperature zone of the nozzle is a constant temperature controlled zone. It is used to achieve the constant temperature requirement of the nozzle. Its setting range is 00% to 99%. If the setting is 99%, 10-30 seconds may be set in the computer as the full-period heating time. If the setting is 20 seconds, it means 20 seconds is one cycle of the thermostatic control.

Example: Setting of the temperature-holding zone: 60%, the cyclic time of the thermostatic control: 20 seconds.

That is to say:

20 x 60%=12 sec The heater of the holding zone of the injection nozzle is in “ON” state

20-12=8 sec The heater of the holding zone of the injection nozzle in “OFF” state.

(3) 	When no temperature control is applied for a certain zone, the temperature of that zone will be set to 0.

    - Setting of the Temperature Deviation (alarm)

For the temperature deviation alarm, there are high and low temperature settings. Refer to screen (02). When either of the deviation settings is exceeded, either the high-temperature or low-temperature alarm will be shown on the screen.

Setting of the high-temperature deviation may be +20℃+90℃.

Setting of the low-temperature deviation may be -20℃-90℃.

    - Setting of the Temperature Preheat Function

For the preheat temperature setting, refer to Picture (02).

Preheat Temperature maintains the temperature settings of all zones at the set preheat temperature percentage.

Example: Setting: -20%, temperature setting: 250℃

250℃(100%-20%)=200℃

If the temperature drops from the set point to 200℃, the corresponding zone will be in the temperature control state.

    - Selection of Fully Automatic, Semi-Automatic or Manual Operation

- If manual operation is to be selected, press  When the power is

switched on, the computer will be in manual-operation state automatically without the requirement of pressing the key again. When it is required to return to manual operation after operating in any other mode or when screen is reset, the above key shall be pressed.

- If semi-automatic operation is to be selected, press  and the machine

will operate in semi-automatic mode. Now, the front safety door may be opened and closed every cycle to confirm the operation of the next cycle. Please note that the power supply of the oil pump will be automatically cut off when the rear safety door is opened.

- If fully-automatic operation is to be selected, press  and the machine

will operate in fully-automatic mode. The operator may confirm the operation of the next cycle by selecting the cycle re-start time, photo call sensor or robot resetting.

Only one of the above three modes may be selected at a time. Before selection, the setting of moulding conditions shall be completed and all operating items of the cycle shall be confirmed. In case that the LED of any of the three keys is flashing, it means the data in the computer is locked and can’t be changed. As for the locking and unlocking methods, consult the professional personnel of the client’s plant in charge of data modification.

3.6.5	Setting of Position, Speed and Pressure Data

(1) 	Select the correct keys for the required operation by making use of the screen. When the key for the required operation is pressed, the corresponding screen is shown for setting or modification at once. (As for detailed operation, refer to related picture in Section 3.2).

(2) 	Setting of the position data either by optical encoder parameters (P) or stroke settings (mm) may be used for this purpose. When the stroke is set, the corresponding optical encoder figures may be automatically obtained through conversion by the computer.

(3)	When the function screen is shown and no further changes are to be made by

the operator, press  or or and the normally

operation screen will automatically be shown. In semi-automatic or fully-automatic operation, if none of the keys are pressed, the normally-operating screen will return to the montior within 30 seconds.

3.6.6	Setting of the Numeric Data for Moulding Conditions

When setting moulding conditions, it is necessary to enter the data of such items as the optical decoder, position, stroke, speed, pressure, timers and counters. For digital input of this data, move the cursor to the position of the figures requiring change and enter the correct data. If the entered data is not correct, warnings as to the scope of the data to be entered will appear on the screen as well as new data

prompts. Now the next data change can be made only after pressing  Some

of the numeric keys serve as double-function keys. If any of these keys is directly

and individually pressed, a figure is entered. If  and a numeric key are

pressed simultaneously, the numerical key performs the second function, which is shown on the top of that key. Refer to the description of operation in Chapter 1.

3.6.7	Adjustment of Proportional Numerical Control

Sophisticated proportional adjustment is applied to control the speed and pressure of operation of the machine. The use of percentage speed and pressure greatly facilitates recording and future readjustment.

Numeric control of the speed and pressure is effected by the computer, which provides different current values to control the proportional pressure valve and proportional flow valve in the hydraulic circuit for different operations.

When the pressure ranges between 20kg/cm2 and 145kg/cm2, the corresponding setting range of the working current of the proportional pressure valve is 200mA to 800mA.

The setting of the working current of the proportional flow valve (speed valve) ranges between 200mA and 680mA.

- Closed-loop control

When closed-loop control system IC is used, the machine shall be equipped with system pressure transducer and proximity switches for checking the speed of the screw. In this mode, the computer may automatically linearize the speed and pressure of the machine and record the linearity data.

Linearization of the speed and pressure shall be carried out separately by the methods covered in screen (46) and (47). The computer will carry out the next operation only after such linearization has been completed.

(2)	Open-loop control

In normal cases, open-loop control mode is applied. In such mode, numeric control can only be adjusted manually.

The linearization of speed and pressure shall be effected by the methods described in Section 3.2.38.

On the I/O board card of the computer, the adjustable potentiometer VR1 is for linearizing the maximum pressure output, 99% and VR2 is for linearizing the zero pressure ouput, 0%. Similarly, VR3 is for linearizing the maximum speed output, 99% and VR4, for linearizing the zero speed output, 0%.

3.6.8	Enable and Disable the Key Lock Function

- Press  and  and there will be no change in the screen that is

shown. However the LED at the upper left corner of will flash.

This means the key lock has been activated and no machine computer data will be allowed to be changed.

- Press  and  and there will be no change in the picture that is

shown either. However the LED at the upper left corner of does not flash.

It means that now the keylock function is off and the computer data may be changed in accordance with the requirements.

(3) 	The locking function is provided for the purpose of protecting the data of the machine from being changed willfully by any non-qualified person so as to ensure the quality of products.

3.6.9	Description of Application of the Computer’s Internal Counters

| No. | Function | Description |
| --- | --- | --- |
| C00 | No. of mouldings | No. of moulding setting |
| C01 | No. of reject mouldings | No. of reject moulding setting |
| C02 | Production time | Total time required by production, Unit: 0.1 hour |
| C03 | Production batch | Reserved function |
| C04 | Ejector cycle | No. of the ejector cycle setting |
| C05 | Ejector vibration | Setting of no.of ejector vibration times i.e. the back and forth vibration times of the ejector after ejection |
| C06 | Unscrewing forward cycles | Setting of the total turn number of moving forward No.of unscrewing forward revolutions setting |
| C07 | Unscrewing backward cycles | No. of unscrewing backward revolutions setting |
| C08 | Lubrication | Settings of intervals (no, of moulding cycles) and times of automatic lubrication |
| C09 | Reserved function |  |
| C10 | Reserved function |  |
| C11 | Reserved function |  |
| C12 | Reserved function |  |
| C13 | Reserved function |  |
| C14 | Reserved function |  |
| C15 | Reserved function |  |

3.6.10	Description of Application of the Computer’s Internal Timer

| No. | Function | Description |
| --- | --- | --- |
| T00 | Injection time | Total injection time, not including the holding time |
| T01 | Cooling time | Under “Auto” mode, the time interval between end of injection and mould opening |
| T02 | Recycle time | Under :”Auto” mode, the time interval between end of ejection and the start of nest mould closing |
| T03 | Plasticizing delay | The time delay interval between the end of injection and the start of next plasticizing motion |
| T04 | Pre-plasticizing decompression | Reserved function |
| T05 | Cycle alarm | Cycle time alarm |
| T06 | Low-pressure alarm` | The allowed time interval between the start of low pressure clamping and the actuation of high pressure |
| T07 | Ejection delay | After end of mould opening, the time allowed for ejection |
| T08 | Reserved function |  |
| T09 | Injection hold stage 1 | Injection hold stage1 time interval |
| T10 | Injection hold stage 2 | Injection hold stage 2 time interval |
| T11 | Ejector forward stop | During automatic ejection, the time allowed for the ejector to stop at the forward position before its retraction |
| T12 | Core pull 1 forward time | Core pull 1 forward time |
| T13 | Core pull 1 backward rime | Core pull 1 backward time |
| T14 | Unscrewing 1 forward time | Unscrewing forward time |
| T15 | Unscrewing 1 backward time | Unscrewing backward time |
| T16 | Unscrewing 1 slow forward | Unscrewing slow forward time |
| T17 | Unscrewing 1 slow backward | Unscrewing slow backward time |
| T18 | Nozzle backward | Nozzle backward time |
| T19 | Motor start | Motor Y ( ( time |
| T20 | Reset origin | Reset origin time at manual mode |
| T21 | Moulding blow down | Reserved function |
| T22 | Alarm interval | Alarm buzz interval setting |
| T23 | Alarm cycle | Alarm cycle setting |
| T24 | Limit switch alarm | Limit switch inspection time, injection unit forward, ejector forward, ejector backward, core pull, unscrewing, mould clamping, mould-opening motions etc. |
| T25 | Mould-open venting | After end of mould opening, the time delay setting before the start of ejector forward motion |
| T26 | Mould close delay | Under “Auto”condition the time delay setting after mould clamping |
| T27 | Ejector delay | Time interval between ejector forward and ejector backward |
| T28 | Core pull delay | Time setting for return to initial position |
| T29 | Unscrewing delay | Reserved function |
| T30 | Lubrication time | Lubrication oil supply time setting |
| T31 | Lubrication alarm | Lubrication oil supple alarm time setting (optional function) |
| T32 | Resin barrel colour change | Reserved function |
| T33 | Core pull 2 forward time | Core pull 2 forward time |
| T34 | Core pull 2 backward time | Core pull 2 backward time |
| T35 | Nozzle fast forward | Nozzle unit fast forward time setting, which equals to half of set value of TIM8 |
| T36 | Mould-open pressure release | Reserved function |
| T37 | Accumulator time delay | When using accumulator assisted injection, the accumulator discharge delay time during injection |
| T38 | Reversed function | Reserved function |
| T39 | Reversed function | Time of interval between the different motions |
| T40 | Core pull 3 forward time | Core pull 3 forward time |
| T41 | Core pull 3 backward time | Core pull 3 backward time |
| T42 | Unscrewing 2 forward time | Unscrewing 2 forward time |
| T43 | Unscrewing 2 backward time | Unscrewing 2 backward time |
| T44 | Unscrewing 2 slow forward | Unscrewing 2 slow forward |
| T45 | Unscrewing 2 slow backward | Unscrewing 2 slow backward |
| T46 | Air blow 1 | Air blow 1 time |
| T47 | Air blow 2 | Air blow 2 time |
| T48 | Reserved function | Aux |
| T49 | Reserved function | Aux |

3.6.11	Description of Input and Output Port of the Computer

| No. | Function | Description |
| --- | --- | --- |
| I00 | Input port | Front safety door |
| I01 | Input port | Rear safety door |
| I02 | Input port | Safety door LS (limit switches) |
| I03 | Input port | Nozzle forward LS |
| I04 | Input port | Core pull 2 forward LS |
| I05 | Input port | Core pull 2 backward LS |
| I06 | Input port | Unscrewing 1 forward LS |
| I07 | Input port | Unscrewing 1 backward LS |
| I08 | Input port | Core pull 1 forward LS |
| I09 | Input port | Core pull 1 backward LS |
| I10 | Input port | Photoelectric sensor |
| I11 | Input port | Accumulation charging ending |
| I12 | Input port | Robot take-arm arm interlock |
| I13 | Input port | Ejector enable |
| I14 | Input port | Take-out completed |
| I15 | Input port | Unscrewing 1 displacement |
| I16 | Input port | Mould adjust overload |
| I17 | Input port | Pump overload |
| I18 | Input port | Mould adjust forward limit |
| I19 | Input port | Mould-adjust backward limit |
| I20 | Input port | Mould-adjust displacement |
| I21 | Input port | Lubrication oil level |
| I22 | Input port | Lubrication pressure |
| I23 | Input port | Low pressure sensor (for standard machine) Rear door (left) (for CE Mark) |
| I24 | Input port | Rotary gate in LS |
| I25 | Input port | Rotary gate out LS |
| I26 | Input port | Low pressure clamping |
| I27 | Input port | High pressure clamping |
| No. | Function | Description |
| I28 | Input port | Mould clamping end position |
| I29 | Input port | Pressure release completed |
| I30 | Input port | Mould clamping extreme limit LS |
| I31 | Input port | Mould opening extreme limit LS |
| I32 | Input port | Mould clamping preset |
| I33 | Input port | Injection preset |
| I34 | Input port | Ejection preset |
| I35 | Input port | Door open end LS |
| I36 | Input port | Door-clos end LS |
| I37 | Input port | Oil filter |
| I38 | Input port | Unscrewing 2 forward LS |
| I39 | Input port | Unscrewing 2 backward LS |
| I40 | Input port | Nozzle guard |
| I41 | Input port | Hydraulic mould fixing |
| I42 | Input port | Oil temperature alarm |
| I43 | Input port | Dirty oil discharge |
| I44 | Input port | Heater hand faulty |
| I45 | Input port | Core pull 3 forward LS |
| I46 | Input port | Core pull 3 backward LS |
| I47 | Input port | Unscrewing displacement |

| No. | Function | Description |
| --- | --- | --- |
| O00 | Output port | Mould adjust forward |
| O01 | Output port | Mould adjust backward |
| O02 | Output port | Mould clamping |
| O03 | Output port | Nozzle forward LS |
| O06 | Output port | Injection |
| O05 | Output port | Plasticizating |
| O06 | Output port | Decompression |
| O07 | Output port | Nozzle backward |
| O08 | Output port | Mould open |
| O09 | Output port | Ejector forward |
| O10 | Output port | Ejector backward |
| O11 | Output port | Extra fast |
| O12 | Output port | Core in 1 |
| O13 | Output port | Core out 1 |
| O14 | Output port | Unscrewing 1 forward |
| O15 | Output port | Unscrewing 1 backward |
| O16 | Output port | Accumulator charging |
| O17 | Output port | Accumulator discharging |
| O18 | Output port | Air blow 1 |
| O19 | Output port | Air blow 2 |
| O20 | Output port | Back pressure mold opening |
| O21 | Output port | Extra fast |
| O22 | Output port | Reserved function |
| O23 | Output port | Reserved function |
| O24 | Output port | Automatic door open |
| O25 | Output port | Automatic door close |
| O26 | Output port | Reserved function |
| O27 | Output port | Reserved function |
| O28 | Output port | Reserved function |
| O29 | Output port | Unscrewing 2 forward |
| No. | Function | Description |
| O30 | Output point | Unscrewing 2 backward |
| O31 | Output port | Pump start |
| O32 | Output port | Automatic injection |
| O33 | Output port | Mould open completed |
| O34 | Output port | Safety door closed |
| O35 | Output port | Back pressure |
| O36 | Output port | Core in 2 |
| O37 | Output port | Core out 2 |
| O38 | Output port | Lubrication output alarm |
| O39 | Output port | Reserved function |
| O40 | Output port | Core in 3 |
| O41 | Output port | Core out 3 |
| O42 | Output port | Reserved function |
| O43 | Output port | Pump running |
| O44 | Output port | Lubrication output |
| O45 | Output port | Alarm output |
| O46 | Output port | Lubrication oil discharge |
| O47 | Output port | Pump start |

3.7		CH-3.5PC Special Screen Operation

| 1. Language selection and mould No.data initial setting screen (45): |  | Press the keys “Cancel” and “ fast clamp ” simultaneously to start the computer. |
| --- | --- | --- |
| 2. Speed linearization screen (46): |  | Press the keys “Fast open and “ melt decompression” simultaneously to start the computer |
| 3. Pressure linearization screen (47): |  | Press the keys “Slow open” and “Function Selection” simultaneously to start the computer. |
| 4. Speed and pressure adjusting screen (48): |  | Press the keys “Fast clamp” and “holding pressure” simultaneously to start the computer. |
| 5. Mode serial no. and machine No. changing screen: |  | Press the keys “Cancel” and “low-pressure clamping” simultaneously to start the computer. |
| 6. Encoder setting screen(28): |  | 3 seconds after pressing the keys “Cancel” and “high-pressure clamp ” simultaneously |
| 7. Auxiliary speed and pressure screen (30): |  | 3 seconds after pressing the keys “Cancel” and “Mould-Adjustment” simultaneously. |
| 8. Ramp up and down screen (29): |  | 3 seconds after pressing the keys “Cancel” and “Injection” simultaneously |
| 9. Delay timer screen (21): |  | 3 seconds after pressing the keys “Cancel” and “Timer” simultaneously |
| 10. Timer monitoring (42,43): |  | 3 seconds after pressing the keys “Cancel” and “5” simultaneously. |
| 11. Ladder program monitoring screen (33): |  | 3 seconds after pressing the keys “Cancel” and “7” simultaneously |
| 12. Counter monitoring screen (44): |  | 3 seconds after pressing the keys “Cancel” and “2” simultaneously |
| 13. Input and output monitoring screen (34-39): |  | 3 seconds after pressing the keys “Cancel” and “8” simultaneously. |
| 14. Input and output status screen (40,41) |  | 3 seconds after pressing the keys “Cancel” and “9” simultaneously. |
| 15. Nozzle unit setting screen (16): |  | Press the keys “Cancel” and “Function Selection” simultaneously |
| 16. Adjustment function screen (22): |  | Press the keys “Cancel” and “Lubrication adjustment” simultaneously. |
| 17. Temp alarm screen (04): |  | Press the keys “Cancel” and “Temperature” simultaneously. |
| 18. Quality statistics screen (25): |  | Press the keys “Cancel” and “Statistics” simultaneously |
| 19. Pressure setting screen(27) |  | Press the keys “Cancel” and “Pressure” simultaneously |
| 20. Injection graph screen (26) |  | Press the keys “Cancel” and “graph” simultaneously. |
| 21. Mould No. copying picture (24): |  | Press the keys “Cancel” and “Mould No./Copying” simultaneously |
| 22. Mould No. selection picture (23): |  | Press the key “Mould No/Copying”. |
| 23. Lubrication setting picture (18): |  | Press the key “Lubrication/Copying”. |

3.8		CH-3.5 PC Standard Electrical Wiring Diagram

# Text boxes

Figure 3.8.4

Figure 3.8.1

Figure 3.8.2

Figure 3.8.3

Figure 3.8.5

Figure 3.8.6