# MPC40 Multifunction Computer

Imported from Japan, MPC40 PC is compliance with al types of JIS inspection standards. Equipped with a 10.4 inch (640 x 480) colorful extra-large LCD screen, it has a wide operating voltage range: AC 110V~AC 280 V 50/60 Hz, plus ultra high stability. The data stored can be kept for 5 years or above under the condition of power failure.

Chinese, English or Japanese language can be freely selected and they can be switched over from one to the other, facilitating learning to operate the computer.

# Features:

- Enlarged memory which may store 150 sets of mold information (e.g. time, counting times, pressure, speed, stroke, quantity, mold thickness, explanation of mold number, conditions for selection, barrel temperature. All data can be stored either in floppy disk or PC alternatively

- Data lock function prevents unauthorized access and mistaken amendment.

- Detailed online operation instruction and multiple user management.

- Temperature holding of nozzle: heating time setting for the nozzle with up to 100% temperature being maintained, or control in PID way.

- 8-stage PID temperature control with an adjusting range of 30℃－500℃, with K type thermocouple.

- Cold start prevention, automatic preheat function.

- Alarm setting on the control of high and low oil temperature and breakage of the thermocouple cable during running is available.

- Automatic detection of blocked nozzle and material overflow

- 10-stage injection speed, 10-stage injection pressure and 10-stage holding pressure.

- 10-stage plasticising speed, 10-stage plasticising pressure and 10-stage backpressure.

- 3-sets air-blow ejection setting and 3-sets core pulling setting

- High-accuracy electronic linear transducer used for clamping, injection and ejection.

- Data input error prevention and prompting.

- Production volume setting for auto-stop function

- Super lubrication setting for toggle unit, setting of the frequency of lubrication form mechanical links and alarm for lacking in oil.

- Operation diagram display for monitoring operating process of the plastic injection machine

- Diagnostic function can check the status of 48 input devices, 48 output devices, as well as monitoring 100 timers and 32 counters.

- Mold data can be overwritten or deleted freely. Default mold data can be selected to save time.

- Using the latest advanced SMT (Surface-Mounting Technology) for the I/O board.

- Using two 32 bits Intel IC.

MPC40 is a new generation product of Chen Hsong with even more powerful function. Comparing with CH-3.8PC, MPC40 is equipped with newer hardware and more enhanced software.

| Function | MPC40 | CH3.8PC |
| --- | --- | --- |
| LCD display | 640×480 | 320×240 |
| Plasticising control | 10-stage speed, pressure, back pressure and free switch over | 2-stage speed, pressure, back pressure control |
| Injection control | Holding 10-stage speed, pressure and back pressure settings | Holding 5-stage injection speed and pressure, 2-stage back pressure settings |
| Opening/clamping control | 5-stage speed and 5-stage pressure | 3-stage speed and 3-stage |
| Positioning control | 4-channel linear input (clamp/injection/ejector/injection chassis) | 3-channel encoder input (clamp/injection chassis/ejector) |
| Gas-assisted injection | With 6-stage pressure control | Order-made program. |
| Real time clock control | Provide clock for preheating control, historical alarm information, and etc. | No |
| Proportional voltage output | PWM x 4 and 10 bit D/A x 4 | PWM x 4 and 10 bit D/A x 3 |

Notes: All functions that are described in the instruction manual are not necessarily equipped in the machine. The function of the machine is determined by the standard configuration of the model plus the purchased option device.

Index

3.1	Introduction on the computer panel

| 3.1.1 | Diagram of the computer panel | ……… | 4 |
| --- | --- | --- | --- |
| 3.1.3 | Forming condition control button | ……… | 6 |
| 3.1.3 | Forming condition numeric data button | ……… | 6 |
| 3.1.4 | Manual operation button and instruction | ……… | 8 |
| 3.1.5 | Power switch | ……… | 8 |

3.2	Instruction on the computer operation screen

| 3.2.1 | Power on test | (00) Screen | ……… | 9 |
| --- | --- | --- | --- | --- |
| 3.2.2 | Running and temperature setting | （01）Screen | ……… | 10 |
| 3.2.3 | Temperature and temperature discrepancy alarm setting | （02）Screen | ……… | 11 |
| 3.2.4 | Opening/clamping parameter setting | （03-04）Screen | ……… | 12 |
| 3.2.5 | Ejection and blow | （05-06）Screen | ……… | 14 |
| 3.2.6 | Core and unscrew | （07）Screen | ……… | 17 |
| 3.2.7 | Injection setting | （08）Screen | ……… | 19 |
| 3.2.8 | Barrel setting | (09) Screen | ……… | 21 |
| 3.2.9 | Injection/barrel stage setting | (10) Screen | ……… | 23 |
| 3.2.10 | Gas-assisted injection and multi-group pump | (11) Screen | ……… | 24 |
| 3.2.11 | Mold adjustment setting | (12) Screen | ……… | 25 |
| 3.2.12 | Injection chassis and auto clearing setting | (13-15) Screen | ……… | 26 |
| 3.2.13 | Initial data setting | (16-23) Screen | ……… | 29 |
| 3.2.14 | Forming mold no. and time setting | (24) Screen | ……… | 41 |
| 3.2.15 | Mold no. selection and mold no. overwriting | (25) Screen | ……… | 42 |
| 3.2.16 | Quality record setting | (26-27) Screen | ……… | 43 |
| 3.2.17 | Diagrams of injection | (28-32) Screen | ……… | 45 |
| 3.2.18 | Program status test | (33) Screen | ……… | 50 |
| 3.2.19 | Input and output test | (34-35) Screen | ……… | 51 |
| 3.2.20 | Status test | (36) Screen | ……… | 53 |
| 3.2.21 | Timer test | (37-39) Screen | ……… | 54 |
| 3.2.22 | Counter test | (40) Screen | ……… | 57 |
| 3.2.23 | Language selection and clock setting | (41) Screen | ……… | 58 |
| 3.2.24 | Historical alarm | (42) Screen | ……… | 59 |
| 3.2.24 | Help | (43) Screen | ……… | 60 |
| 3.2.26 | Notes on password | (44-48) Screen | ……… | 61 |

3.3 Introduction on the computer alarm

3.1		Introduction on the computer panel

3.1.1	Computer panel

3.1.2	Forming condition control button

The keyboard has the following function:

- Select the forming operation status

- Able to set the location, speed, pressure, time and counter in the forming condition

- Able to set the data needed by the auto mold adjustment

- Able to amend the mold and overwrite the mold no.

- Able to select the function or movement that are needed in the forming as per the need of product and die design

- Able to press to move to the intended location for data amendment under any operation screen

- Mold and auto door operation share the same button. When using the mold adjustment function, you need to switch to the mold adjustment screen at first. (refer to the second chapter for notes)

3.1.3  Forming condition numeric data button

The keyboard has the following function

(1)	Input the numeric data that is needed in the forming condition

Speed setting range: 00~99, when setting as 00, the speed is zero

Pressure setting range: 00~99, when setting as 00, pressure is zero

Location setting range: 0000~999.9mm

Time setting range: 0~6553.5 sec

Counter setting range  0～65535。

Mold thickness value range 0～6553.5 mm。

(2) Able to check if the keyboard functions normal or not

(3) Able to read the computer control program

(4) Notes for each button

： Number “0” or blank text

： Number “1” or letter “S”, “T”, “U”

： Number “2” or letter “V”, “W”, “X”

：Number “3” or letter “Y”, “Z”, “_”

： Number “4” or letter “J”, “K”, “L”

： Number “5” or letter “M”, “N”, “O”

： Number “6” or letter “P”, “Q”, “R”

： Number “7” or letter “A”, “B”, “C”

： Number “8” or letter “D”, “E”, “F”

： Number “9” or letter “G”, “H”, “I”

： Reconfirm the data input

： Turn the function on or increase the value by “1”

： Turn the function off or decrease the value by “1”

： Data input

： Adjust the contrast

： Move the cursor to the left

： Move the cursor downward

： Move the cursor to the right

： Move the cursor upward

3.1.4	 Manual operation buttons and notes

- The manual operation keyboard can independently manipulate a single movement in the whole cycle

    - Power switch

- Emergency stop button

This red button is located in the right bottom of the operation panel of the computer. Press this button to power off the machine. To restart the machine, you need to rotate the button as per the direction of the arrow to loosen the button.

(2) Start-up button

This green button is located below the emergency stop button. Press this button to power on the control unit of the machine. This function can effectively protect the computer system.

(3) There is a high performance manostat within the machine, which is able to beat the voltage input ranging AC90V – AC265V 50/60HZ

3.2	Instruction on the operation screen

3.2.1 Power on test

Screen 00

- Screen (00) appears when the system runs an auto test after power on. This screen shows the machine model, machine no. program, and etc. It is automatically switched to the running screen after 3 seconds.

- In case of maintenance or technical inquiry is needed, please advise the machine model, machine no. and program shown above to the customer service staff to obtain fast service.

3.2.2	Running and temperature setting

Screen 01

Screen (01) is displayed when running

If you press button or button or button, then screen (01) will also be brought forward. You can find various parameters such as filling time, cycle time, formed no., temperature in each stage, and the current operation of the machine. You can also set the injection time, cooling time, and the recycle time by moving the cursor to the corresponding location with  button and input the intended time with the numeric button, followed by pressing button to complete the modification.

When you activate the parameter to be modified with the cursor button . The maximum and minimum value of the parameter will be prompted on the screen.

When you activate the function to be modified with the cursor button . The buttons to be needed to press will be prompted on the screen.

3.2.3 Alarm setting on temperature and temperature discrepancy

Screen 02

Press  button to bring forward the screen (02). Screen (01) and screen (02) can be freely switched over. In screen (02) as shown above, from the left to the right there are setting on nozzle temperature, 1st stage temperature, 2nd stage temperature, 3rd stage temperature, 4th stage temperature, 5th stage temperature (as needed by the tonnage of the machine), 6th stage temperature (as needed by the tonnage of the machine) and oil temperature. In the setting of each stage temperature, there is alarm setting on the maximum and minimum value. The maximum value can be set to +50 and the minimum value –50. In addition, MPC40 has the function of holding temperature, and setting the time daily for starting the temperature holding.

The setting methods of various function and parameters are as below,

Press  button to activate the parameter to be modified, then input the intended value and press  to complete. When one parameter is activate, the input range of it will be shown at the bottom of the screen.

The temperature holding function and daily temperature starting function can be activated by press  button to get activated, followed by press or  button to select enable or disable the function.

3.2.4	 Parameter setting for opening/clamping

1、Parameter setting

Screen 03

- Press  or  button to call up screen (03), in which you can set the speed, pressure and location for all stages of opening/clamping mold

- The minimum and maximum stage of mold open is 3 and 5 respectively. 3 stages mean slow, fast and decelerate. 5 stages mean slow, 2nd stage, 3rd stage, fast and decelerate.

Similarly, the minimum and maximum stage of mold clamp is 3 and 5 respectively. 3 stages mean fast, low pressure and high pressure. Press cursor button  to select the parameter setting for mold opening/clamping. Input the intended value followed by pressing  button to complete the setting.

2、Accelerate and decelerate setting

Screen 04

（1）Press  +  button in screen 03 to call up screen 04, in which you can made setting on the accelerate and decelerate parameter in mold opening/clamping.

（2）The stages of mold opening/clamping can be set here. The maximum and minimum stages are 3 and 5 respectively.

（3）The speed pressure parameter for accelerate/decelerate means the time to be consumed to reach the movement.

（4）To modify the setting, press  button to activate the parameter first, then input the intended value followed by pressing  button to complete the setting.

3、Notes on mold open/clamp time

<1> Notes on mold open time

←──── ←────←──── ←────←────

↑              ↑               ↑               ↑             ↑

<2> Notes on mold clamp time

←─	 		                                 	 ─→

────→ ────→ ────→────→ ────→

3.2.5 Ejection and air blow

1、Parameter setting

Screen 5

- Press  to call up screen (05). You can set various parameters for ejection and blow.

- Press cursor button  to select the parameter setting for ejection and blow, input the intended value followed by pressing  button to complete the setting.

- Press  button to set the movement style of ejector

（1）No move

（2）Ejector stop

（3）Multiple ejection

（5）Time setting for ejector stop TIM11 (0~99.9 seconds)

- Times of ejection CNT04 (0~99 times)

- Press cursor button  to select ejector forward 1, ejector forward 2, ejector backward or ejector decelerate and etc. Input the intended value followed by pressing button to complete the setting.

- Notes for ejector location

Ejector moves forward

Ejector forward position 1       Ejector forward position 2

∨                 ∨

Ejector moves 	forward 1 (speed and pressure)  Ejector moves 	forward 2 (speed and pressure)

───────────────────→ Ejector stops

Backward stops←────────	←──────────

Ejector decelerates      	      	  Ejector moves backward

Ejector moves backward

- Press cursor button  to select blow setting. Input the intended value followed by pressing  to complete the setting.

（1）You can turn on or off the “Blow movement 1” by pressing  or  to make the setting. This operation starts until the completion of mold open.

Blow time 1: time needed for blow 1

Blow delay 1: time delayed for blow after mold open

（2）You can turn on or off the “Blow movement 2” by pressing  or  to make the setting. This operation starts during mold open.

Mold position when blow 2 starts: set the start position of blow 2 during mold open

Blow time 2: time needed for blow 2

Blow delay 2: time delayed for the start of blow 2 after mold positioning.

（3）You can turn on or off the “Blow movement 3” by pressing  or  to make the setting. This operation starts during mold open.

Mold position when blow 3 starts: set the start position of blow 3 during mold open

Blow time 3: time needed for blow 3

Blow delay 3: time delayed for the start of blow 3 after mold positioning.

2、Setting for ejector accelerate/decelerate

Screen 06

（1）Press  + in screen 05 to enter the password inputting screen. Screen 06 will be called up after the correct password is input, in which you can make settings on the ejector accelerate/decelerate parameters.

（2）调节该两项参数，即可调整帝国内政动作的斜率。

You can set the add/minus parameter for the ejector and mold adjustment ejector. The mold adjustment ejector is a special function.

（3）Press the cursor button  to select the parameter that needs to be modified. Input the intended value followed by pressing  to complete the setting.

3.2.6 Core and unscrew

Screen 07

（1）Press  to call up the screen 07

（2）Within this screen, you can set the parameters for three groups of core. Press  to activate the parameter, then input the intended value followed by pressing  to complete the setting.

（3）For the 1st group you can set as Core 1, Unscrew 1, No move. Press  or  to select.

（4）”Move Style”: Press  to select within the following three modes: “Time”, “Count” and “Limited Position”, of which “Count” is only valid in case of Unscrew.

（5） “Sync Move”: Press  to select within the following two modes: “On” and “Off”

（6） “Hold”: Press  to select within the following two modes: “On” and “Off”

- Core 1 forward position: the position that Core 1 or Unscrew 1 starts to fill core

- Core 1 backward position: the position that Core 1 or Unscrew starts to retreat core

- Setting on forward 1 speed, pressure or time

Speed: 0％～99％

Pressure: 0～999bar

Time: 0～99.9 seconds

- Setting on backward 1 speed, pressure or time

Speed: 0％～99％

Pressure: 0～999bar

Time: 0～99.9 seconds

- The settings for the other two groups are the same of that of the first group.

3.2.7 Injection settings

Screen 08

（1）Press  to call up screen (08). Press the cursor button  to select the setting for injection. Input the intended value followed by pressing  to complete the setting.

- Injection time: 0～999.9 seconds

- Three modes for holding-pressure switch: “Time” “Location” and “Pressure”

（4）0～999bar

（5）Pressure holding stages: 10 stages in total

Speed: 0~99%. The speed for each stage can be set independently.

Pressure: 0~999bar.The pressure for each stage can be

set independently.

Time: 0~99.9 seconds. The pressure holding time for each stage can be set independently.

（6）Injection stages

Speed: 0~99%. The speed for each stage can be set independently.

Pressure: 0~999bar.The pressure for each stage can be set independently.

Position: 0~1999.9mm. The position for each stage injection can be set independently.

（7）“Release the holding pressure”: Press  to select to enable or disable to release the holding pressure.

- Time for holding pressure and injection

←────   TIM 0  Injection time TIM 0─────→

←── ←─── ←─── ←─── ←───

↑       ↑       ↑        ↑       ↑

Overflow

←─── ←─── ←──── ←─── ←────

↑       ↑        ↑        ↑        ↑

←─── ←─── ←──── ←─── ←────

↑       ↑        ↑        ↑        ↑

←─── ←─── ←─── ←───  ←─── ←───

↑       ↑        ↑        ↑        ↑

3.2.8 Plasticization setting

Screen 09

（1） There are 10 stages in total in plasticization, each of which has four parameters, including speed, pressure, back pressure and location. To set the parameter, press  to call up screen (09). Then press the cursor button  t select the plasticization settings. Input the intended value followed by pressing  to complete the setting.

（2）Notes on various parameters:

Speed 0～99％

Pressure: 0～999bar (maximum value of the system)

Back pressure: 0～999bar (maximum value of the system)

Location: 0～1999.9mm (the position that the current stage of plast ends)

Backward injection: Speed （0～99％）, Pressure （0～999bar）, Stop position （0～999.9mm）

Backward injection before plast: You can press  or  to enable or disable the function. In the “On” status, the time setting can be 0～999.9 second.

Plasticising time delay: 0～99.9 seconds

Alarm break: 0～999.9 seconds

- Notes on different stage of time of plast

───→ ───→ ───→ ───→ ───→ ───→

←─Stroke of screw backward move─→

───→ ───→ ───→ ───→ ─────────→

↑      ↑       ↑       ↑       ↑                  ↑

3.2.9 Setting on stages of injection/plast

Screen (10)

(1) In screen 09, press  + to call up the screen 10, within which you can make settings on injection/plast stage and accelerate/decelerate

(2) The stage of injection, holding pressure and plast can be set in screen 10. You can set for 10 stages at most.

(3) The pressure parameter of accelerate/decelerate refers to the time that is consumed to reach the move.

(4) To make setting on the parameter, press  button to activate the parameter to be modified, then input the intended value followed by pressing  to complete the setting.

3.2.10	Gas-assisted injection and multiple group pump

图11 Screen 11

（1）The function of gas-assisted injection/multiple group pump is newly added in MCP40. Press + in screen 10 to call up the password input screen, and then input the correct password and press + twice to call up screen 11.

（2）By pressing or, you can enable or disable the gas-assisted injection function. In the “On” status, you can set the gas-assisted time and gas-assisted stop location. To set the parameter, press  to active the parameter, and then input the intended value followed by pressing  to complete the setting.

（3）At the same time, we can set 6 group of pump for spare use. You can set the speed or pressure (0~99%) and working time (0~99.99 seconds) for each pump. You can press  button to activate the parameter, and then input the intended value followed by pressing  to complete the setting. (Optional)

3.2.11 Mold adjustment setting

Screen 12

（1）Press  to call up the screen 12

- Auto mold adjustment: Press the cursor button  to active the setting. Press  or  to enable or disable the auto mold adjustment function

- Teeth mold adjustment: Press the cursor button  to active the setting. Press  or  button to enable or disable the single teeth mold adjustment function. This function is optional.

- Mold thickness selection: 0～6553.5mm. Press the cursor button  to active the setting, then input the intended mold thickness value followed by pressing  to complete the setting.

- The setting for mold adjustment speed (0~99%) and pressure (0~999bar) can be activated by pressing the cursor button , then input the intended value followed by pressing  to complete the setting.

3.2.12 	Injection chassis and auto clearing setting

1、Parameter setting

图13

- Press  or  or  to call up the screen (13)

- Press  button to select the parameter, input the intended value followed by pressing  button to complete the setting.

Of which there are:

Injection chassis movement: there are three styles including before plast, after plast and fixed, the setting of which can be achieved by pressing  or  button.

The “Auto Clearing” function can be enabled or disabled, which can be achieved by pressing  or  button.

Various movements including fast chassis, slow chassis, chassis backward, injection, plast, injection backward can be determined by three parameters including speed, pressure, and location. The value shown in the screen is the maximum value.

The “Auto Clearing” function is determined by two parameters “Times” and “Time”.

（3）Other data shown in the screen are tested data by the computer.

（4）

2、Setting on accelerate/decelerate

图（14）Screen (14)

- In the chassis screen, press  +  to call up the screen (14)

- Press  button to select the parameter to be modified, then input the intended value followed by pressing  button to complete the setting.

Of which there are:

The speed and pressure parameter behind the chassis refers to the time that is needed by accelerate/decelerate until the chassis reaches the ultimate speed.

The speed and pressure parameter behind the mold adjustment chassis refers to the speed and pressure that the chassis reaches in the end.

3、Setting on backup speed and pressure

Screen (15)

- Press +chassis to call up the screen (15)

- Press  button to select the parameter to be modified, input the intended value followed by pressing  button to complete the setting.

3.2.13 Setting on initial data

1、Use of special function

Screen 16

- Press + mould open to enter the password screen, input the correct password, then press + to enter the screen (16)

- Press  to select the function

Of which there are:

Lubrication style: three styles including “Spare”, “Time” and “Switch”. Press  or  to make settings.

Chassis movement style: you can choose “Location: or “Time” control. The standard machine uses the “Time” control.

Rear safety door: there are two status, “On” and “Off”, which can be selected by pressing  or button. “On” means to inspect the rear safety door, and “Off” means not to inspect the rear safety door (Optional)

Interlink function: there are two status: “On” and “off”, which can be selected by pressing  or  button (Optional)

Energy saving device: there are two status: “In use” and “Not in use”, which can be selected by pressing  or  button.

Core protection: there are two status: “On” and “off”, which can be selected by pressing  or  button (Optional).

Fast style: there are two status: “Style 1” and “Style 2”, which can be selected by pressing  or  button.

Fast injection: there are two status: “Use” and “Not in use”, which can be selected by pressing  or  button (Optional)

Rear pressure selection: there are two status: “On” and “off”, which can be selected by pressing  or  button.

Top safety door: there are two status: “On” and “off”, which can be selected by pressing  or  button (Optional)

Auto door: there are two status: “Use” and “Not in use”, which can be selected by pressing  or  button.

Photo sensor test: there are two status: “Use” and “Not in use”, which can be selected by pressing  or  button.

Number of pump: The number can be selected by pressing  or  button (Optional).

Special core: there are five status: “Style 1”, “Style 2”. “Style 3”, “Style 4”, “Style 5” and “Not in use”, which can be selected by pressing  or  button.

Injection pressure: there are two status: “Use” and “Not in use”, which can be selected by pressing  or  button (Optional).

This is an optional function.

Plast torque: there are two status: “Use” and “Not in use”, which can be selected by pressing  or  button (Optional).

This is an optional function.

There are three settings: “Manual”, “PID”, and “Not in use” for “Nozzle”, “Temperature 1”, “Temperature 2”, “Temperature 3”, “Temperature 4”, “Temperature 5”, “Temperature 6”, which can be selected by pressing  or  button.

（3）“Tel”, “Fax”, “Machine Model”, “Model number”, “Manufacture Date”: Press the intended value followed by pressing  to completing the setting.

2、Adjust the function setting.

Screen 17

- In screen (16), keep pressing + button to enter screen (17)

- Press  button to select the function, input the intended value followed by press  button to complete the setting.

- The value shown in the screen above is the maximum value of the parameters. The maximum and minimum values that are set here are used to define the parameter setting of various functions under their owing setting screen.

3、Setting on location of mold clamp

Screen (18)

- In screen (17), press + button to call up screen (18), which is the adjust screen of electronic ruler.

- Press  button to select the parameter, input the intended value followed by pressing  button to complete the setting.

Of which there are:

There are three parameters are available for adjustment: “Current”, “Minimum” and “Maximum” for the four function positions, which are “Clamp position”, “Injection position”, “Ejector position”, and “Chassis position”. Each parameter has two values. The left value is the sensor data of the electronic ruler, and the right value is the actual stroke to be needed.

There are three parameters are available for adjustment: “Current”, “Minimum” and “Maximum” for the “Oil pressure” function. Each parameter has two values. The left value is the sensor data of the pressure sensor, and the right value is the actual pressure to be needed.

There are three parameters are available for adjustment: “Current”, “Minimum” and “Maximum” for the “Mold Adjust thickness” function. The “Minimum” parameter refers to the thickness of the thinnest mold that can be installed on the machine. The “Maximum” parameter refers to the thickness of the thickest mold that can be installed on the machine. The “Current” parameter refers to the actual thickness of the mold that is installed on the machine.

（3）  At the bottom of the screen shows the save function. There are two parameters available for adjustment. The first parameter is the store device with two selections “FLASH” and “FD”. The second parameter is the type of parameter that is saved with three selections “ALL”, “LIMIT” and “MOLD COM”. The selection of the parameter can be achieved by pressing the  or  button. In addition there are three function button “SAVE”, “LOAD” and “FD FORMAT”, which can save the data to the storage device, or read the data from the storage device, or format the floppy the disk.

FLASH means to save the current parameters to the storage device of MPC40.

FD means to save the current parameters to the 3.4” floppy disk.

ALL means to select all parameters.

LIMIT means to select the position parameter only.

MOLD COM means to only save the forming condition.

- Data adjustment method for the electronic ruler

In all the parameters above, the mold clamp position, injection position, ejector position and chassis position are corresponding to the electronic ruler. Take the mold clamp position as an example. The adjustment is as below,

    - Set the maximum stroke of the mould clamp position, i.e. as 3000

    - Set the minimum value of the mould clamp position as “0”. Then take the mold clamp position to the end, and read the sensor data f the electronic ruler at the left of the current parameter. Put the data into the input area at the left of the minimum parameter. (In the actual test, to prevent the interference of the electronic noise, the input value should be more than the actual value by 2. For example, if the sensor date of the electronic ruler is 500, then the input should be 502)

    - Set the maximum value: Set the data of the electronic ruler as the maximum at the left to the parameter. (For example as 16383). Set the right parameter as the maximum stroke (For example as 3000), and then open the mold to the end. Read the sensor data of the electronic ruler at the left to the current parameter, and input the value to the input area at the left to the maximum parameter. (In the actual test, to prevent the interference of the electronic noise, the input value should be less than the actual value by 2. For example, if the sensor date of the electronic ruler is 16383, then the input should be 16381)

    - Apply the same procedure to the other parameters. By take the move to the maximum or minimum end you can get the corresponding value.

4、Output revision setting

Screen (19)

（1） In screen (18), press + to enter the screen (19)

- Press  to select the function. Then input the intended value followed by pressing  button to complete the setting.

- The value shown on the screen is the maximum value of the parameter. The maximum and minimum values are used to limit the range of setting of various functions.

- This screen shows the function when the machine makes a linear adjustment

There are four parameters including “speed”, “pressure”, “backup pressure” and “speed 2”. The “speed” parameter is used to adjust the linear function of system flow valve. The “pressure” parameter is used to adjust the linear function of the system pressure valve. The “backup pressure” and “speed 2” are special parameters, which are optional and should be selected as per the function of the machine.

The instruction on the adjustment of the parameters is shown as below,

“Pressure”: This parameter corresponds two parameters. The left parameter is the actual output pressure of the machine. The right parameter is the volume that the computer outputs to the system pressure valve.

To adjust the parameter, set the output pressure value at the bottom as the maximum pressure of the machine, i.e. 175 bar. Then set the speed and pressure of the chassis moving forward. Check if the value in the pressure gauge is the giving value, i.e. 175bar. If not, then change the value corresponding the “output pressure value” until the pressure shown in the pressure gauge matches the given pressure, i.e. 175bar. For the other parameters, just set at a step-by-step reduction by 10% or 20%.

“Speed” parameter: the setting is similar to that of the “pressure” parameter. Set the maximum value first, then reduce step-by-step pro rata. The left parameter is the percentage of the actual output of the machine. The right parameter is the volume that the computer outputs to the system pressure valve.

To adjust the parameter, just set the percentage of the final output as the maximum value (99%). Then set the maximum speed (99%) of a specific stage of plast (i.e. the last stage) in the plast screen. Give a certain pressure (i.e. 50 bar), then start the plast (pasticising) operation. Check if the rotation speed of the gauge matches. Of not, then adjust the right parameter to make it consistent. Set other parameters by a step-by-step reduction at 10% or 20% pro rata.

“Backup pressure” and “speed 2” can be adjusted accordingly, too.

（5）The “multiple oil pump” is an optional function.

5、Setting on various time relay.

Screen 20

  - In screen (19), press + to enter screen (20), which is to set the time of various relay during the control

  - Press  to select the function, input the intended value followed by pressing  button to complete the setting.

  - The values shown in the screen are the maximum value of various parameters. The maximum value and the minimum value that are set here are used to limit the setting range of the parameters of various functions.

6、Setting on the special time relay

Screen (21)

（1）In screen (20), press + button to enter the screen (21), in which you can set the time for the special time relay in the control of the machine.

（2）Press  button to select the function. Input the intended value followed by pressing  button to complete the setting.

- The values shown in the screen are the maximum value of various parameters. The maximum value and the minimum value that are set here are used to limit the setting range of the parameters of various functions.

7、Setting on various counters

Screen (22)

（1）In screen (21), press + button to enter the screen (22), in which you can set various counters in the control of the machine.

（2）Press  button to select the function. Input the intended value followed by pressing  button to complete the setting.

- The values shown in the screen are the maximum value of various parameters. The maximum value and the minimum value that are set here are sued to limit the setting range of the parameters of various functions.

8、 Setting on closed ring control function

Screen (23)

（1）In screen (22), press + button to enter the screen (23), in which you can set the P.I.D parameters in the closed ring function of the machine.

（2） Press  button to select the function. Input the intended value followed by pressing  button to complete the setting.

- The values shown in the screen are the maximum value of various parameters. The maximum value and the minimum value that are set here are sued to limit the setting range of the parameters of various functions.

3.2.14 	Setting on forming and time

Screen (24)

- Press  to call up the screen (24)

（2）Press  button to select the function. Input the intended value followed by pressing  button to complete the setting.

The “set” parameters of various functions can be set, while the “current” parameter is the actual parameter that has been tested by the computer.

The values shown in the screen are the maximum value of various parameters.

3.2.15  Selection on mold number and mold number overwrite

Screen (25)

（1）Press  to call up screen (25)

（2）Press  button to select the function. Input the intended value followed by pressing  button to complete the setting.

Of which, there are:

Find location: there are two locations, which are “computer memory” and “floppy disk”. You can press  or  to select.

During the access operation on the mold number data, you can save the data corresponding to the mold number to the floppy disk. In addition, you can also save the data corresponding to the mold number in the floppy disk to the computer.

3.2.16  Setting on quality statistics

1、Parameter setting

Screen (26)

（1）Press  to call up the screen (26)

（2）Press  button to select the function.

There are two parameters “Standard” and “Offset” available for selection. Input the intended value followed by pressing  to complete the setting.

Each function has two status “Enabled” and “Disabled”. You can press  or  button to select between them.

- There are “Data reset” and “Save” function in the screen. You can press  button to activate the button, then press  button to complete the setting.

2、 Quality statistics display

Screen (27)

（1）Press “Statistics” twice, or press + in screen (26) to call up the screen (27)

（2）The values shown in this screen cannot be modified. They are the parameters that have been tested by the computer.

3.2.17  Screen display of plasticising

1、Screen display of plasticising end

图（28）Screen (28)

- Press  to call up the screen (28)

- The central position 0 is the setting value of position when the 4th stage plasticising ends. The screen display is the ±value that the position when the actual plasticising ends comparing with the position when the 4th stage plasticising ends.

- To clear the screen, you can reset the data in the quality statistics screen.

- The screen display can be printed out by the computer.

- The maximum value of the coordinator in the screen display is 9.9mm, which can be set by inputting the value.

2、 Display of injection pressure curve

Screen (29)

- In screen （28）, press + button to call up the screen (29).

- This screen displays the pressure curve when the injection controlled by position switches to the pressing holding process controlled by time. The left is time control, the right is position control, and the 0 line in the middle is pressure holding switching position.

- This function has two items: “Standard save” and “Standard line display”. The “Standard save” function can define the current curve as the standard curve and save it. The “Standard line display” can read the saved standard line to compare with the actual curve.

- To clear the screen, you can reset the data in the quality statistics screen.

- The screen display can be printed out by the computer.

3、Display of injection speed curve

Screen (30)

- In screen （29）, press + button to call up the screen (30).

- This screen displays the speed curve when the injection controlled by position switches to the pressing holding process controlled by time. The left is time control, the right is position control, and the 0 line in the middle is pressure holding switching position. The maximum value of the speed parameter in the screen is 1999.9mm/s, which can be determined by inputting the intended value.

- This function has two items: “Standard save” and “Standard line display”. The “Standard save” function can define the current curve as the standard curve and save it. The “Standard line display” can read the saved standard line to compare with the actual curve.

- To clear the screen, you can reset the data in the quality statistics screen.

- The screen display can be printed out by the computer.

4、Display of plast back pressure

图（31）Screen (31)

- In screen （30）, press + button to call up the screen (31).

- The position coordinator in the screen refers to the position of the shaft when the plast is in process. The back pressure coordinator refers to the back pressure of the plast.

- This function has two items: “Standard save” and “Standard line display”. The “Standard save” function can define the current curve as the standard curve and save it. The “Standard line display” can read the saved standard line to compare with the actual curve.

- To clear the screen, you can reset the data in the quality statistics screen.

- The screen display can be printed out by the computer.

5、Display of plast speed curve

Screen (32)

- In screen （31）, press + button to call the screen (32).

- The position coordinator in the screen refers to the position of the shaft when the plast is in process. The speed coordinator refers to the speed of the plast.

- This function has two items: “Standard save” and “Standard line display”. The “Standard save” function can define the current curve as the standard curve and save it. The “Standard line display” can read the saved standard line to compare with the actual curve.

- To clear the screen, you can reset the data in the quality statistics screen.

- The screen display can be printed out by the computer.

3.2.18  Program contents and status check

Screen (33)

- Press  to call up the screen (33)

- This is a trapeziform graphics in the computer. When the dot below the status bar is black, it means there is signal. When the dot is with no color, it means there is no signal. You can press  button to scroll the display.

- There is a search function. Just input the circuit node value in the text area next to “OUT”“TIM”“CNT” and press  button. The circuit node to be searched will be shown in the screen.

3.2.19 Inspection on input and output

1、Monitor the input point

Screen (34)

- Keep pressing  button to call up the screen (34)

- This screen shows the status of the input point of the machine. When the dot is black, it means there is signal. When the dot is white, it means there is signal. You can press  button to scroll the display.

2、Monitor the output point

Screen (35)

- Keep pressing  button to call up the screen (35)

- This screen shows the status of the input point of the machine. When the dot is black, it means there is signal. When the dot is white, it means there is signal. You can press  button to scroll the display.

3.2.20  Status monitor

图（36）Screen (36)

- Press  to call up the screen (36)

- This screen shows the status of the internal relay in the program. The location of the dot is “××××” plus the column number. When the dot is black, it means there is signal. When the dot is white, it means there is signal. You can press  button to scroll the display.

3.2.21 	Inspection on the time relay

1、Check on the counter

Screen (37)

- Press  to call up the screen (37)

- This screen can inspect the set value and current value of various time relays. Press  button to scroll the display.

Screen (38)

- Keep pressing  to call up the screen (38)

(2) This screen can check the set value and current value of various time relays. Press  to scroll the display.

Screen (39)

- Keep pressing  to call up the screen (39)

- This screen can check the set value and current value of various time relays. Press  to scroll the display.

3.2.22 	Monitor counters

Screen (40)

- Press  to call up the screen (40)

- This screen can check the set value and current value of various counters. Press  to scroll the display.

3.2.23 	Language setting and clock setting

Screen (41)

- Press + to call up the screen (41)

- Press  button to select the parameter to be modified. Input the intended value followed by pressing  button to complete the setting.

The display is available in three languages: Chinese, Japanese and English. You can press or  to make the setting.

3.2.24 Historical alarm

Screen (42)

（1）Press  to call up the screen (42), which has the records of all previous alarms. Press “Data reset” to delete the records.

3.2.25  Help

Screen (43)

（1）Press  to call up the screen (43), which has some brief instructions on the machine.

3.2.26	Notes on password

（1）This machine is equipped with a strict password protection function, which can prevent unauthorized data change. When the operator wants to make amendment on the important data, the follow screen (38) will show up to require the password input. The password change screen will appear after the correct password is input.

Screen (44)

（2）To allow the authorized operator to modify the data in a convenient way, the password can be removed. Press + to call up the screen (44). After the correct password is input, the screen (45) will appear, which means the password has been successfully removed. No password input will be required for further amendment on the data.

To resume the password protection function, just press + to input the correct password, or just reboot the system.

Screen (45)

Screen (46)

- Password change

Screen (47)

Screen (48)

Press + to call up the screen (47) and input the password. When the screen (48) appears, it means the password has been successfully changed.

3.3 电脑警报字幕说明Introduction on the computer alarm

| RELAY№ | 中国語 | 英語 |
| --- | --- | --- |
| 800 | 800:警报1 | 800:ALARM 1 |
| 801 | 801:警报2 | 801:ALARM 2 |
| 802 | 802:料管温度未达设定 | 802:BARREL TEMP NOT REACH |
| 803 | 803:润滑油量不足 | 803:LUBRICATION OIL NOT REACH |
| 804 | 804: 润滑器排水阀阻塞 | 804:LUBRICATION RELEASE VAVE CLOG |
| 805 | 805:潤滑油漏油或不足 | 805:LUBRICATION OIL PRESS. TOO LOW |
| 806 | 806:油馬達超過負荷 | 806:PUMP MOTOR OVERLOAD |
| 807 | 807:調模馬達超負荷 | 807:MOLD ADJUST MOTOR OVERLOAD |
| 808 | 808:後安全門未関閉 | 808:REAR DOOR NOT CLOSE |
| 809 | 809:前安全門未関閉 | 809:FRONT DOOR NOT CLOSE |
| 810 | 810:調模超出最小尺寸 | 810:MOLD ADJ MIN LIMIT |
| 811 | 811:調模超出最大尺寸 | 811:MOLD ADJ MAX LIMIT |
| 812 | 812:警報３ | 812:ALARM 3 |
| 813 | 813:油馬達未啓動 | 813:PUMP MOTOR NOT START |
| 814 | 814:鎖模行程巳終止 | 814:CLAMP END |
| 815 | 815:開模行程巳終止 | 815:OPEN END了 |
| 816 | 816:開模行程未終止 | 816:OPEN NOT END |
| 817 | 817:頂針行程巳終止 | 817:EJT FOR END |
| 818 | 818:退針行程巳終止 | 818:EJT BACK END |
| 819 | 819:熔膠行程巳終止 | 819:PLAST END |
| 820 | 820:鬆退行程巳終止 | 820:SCREW BACK END |
| 821 | 821:請檢査射咀前進限位 | 821:CHECK NOZ FOR LIMIT |
| 822 | 822:射咀保護蓋未関関 | 822:NOZZLE GUARD NOT CLOSE |
| 823 | 823:射咀孔異物阻塞 | 823:NOZZLE BLOCK |
| 824 | 824:熔膠量不足或溢料 | 824:SHORT SHOT OR OVER SHOT |
| 825 | 825:料斗無料或阻塞 | 825:NO MATERIAL OR BLOCKED |
| 826 | 826:成型模数巳達設定 | 826:CYCLE COUNT COMPLETED |
| 827 | 827:週期時間過長 | 827:CYCLE TIME TOO LONG |
| 828 | 828:請清理模具内異物 | 828:PLEASE CLEAN UP THE MOLD |
| 829 | 829:調模時間過長 | 829:MOLD ADJUST TOO LONG |
| 830 | 830:潤滑中 | 830:LUBRICATION IN PROGRESS |
| 831 | 831:請檢査機械手取出物 | 831:PLEASE CHECK ROBOT FIXTURE |
| 832 | 832:製品確認訊號異常 | 832:TAKE OUT FAILURE |
| 833 | 833:電眼感應片被遮 | 833:PHOTO CUT ALARM |
| 834 | 834:切断電源重新開機 | 834:POWER OFF THEN ON AGAIN |
| 835 | 835:油過濾網阻塞 | 835:OIL FILTER CLOG |
| 836 | 836:循環油度過低 | 836:OIL TEMP TOO LOW |
| 837 | 837:循環油度過高 | 837:OIL TEMP TOO HIGH |
| 838 | 838:自動模具替換中 | 838:AUTO MOLD CHANGE |
| 839 | 839:半螺母位置不對 | 839:NUT CLOSING NOT ALIGN |
| 840 | 840:請檢査抽芯限位開関 | 840:CHECK CORE PULL LIMIT |
| 841 | 841:請檢査旋轉盆限位開関 | 841:CHECK GATE IN/OUT LIMIT |
| 842 | 842:請檢査頂針限位開関 | 842:CHECK EJECTOR LIMIT |
| 843 | 843:請檢査自動門安全閥 | 843:CHECK VALVE FOR DOOR |
| 844 | 844:大油缸未回定位 | 844:BIG CYLINDER NOT LOCATED |
| 845 | 845:開模洩壓異常 | 845:OPEN PRESSURE RELEASE TROUBLE |
| 847 | 847:鎖模力受力中 | 847:CLAMPING IN PROGRESS |
| 848 | 848:蓄壓器充壓異常 | 848:ACC CHARGE ALARM |
| 849 | 849:液壓油油量不足 | 849:OIL LEVEL TOO LOW |
| 850 | 850:調模計數開関故障 | 850:MOLD ADJUST SENSOR TROUBLE |
| 851 | 851:調模齒輪異常檢査 | 851:MOLD ADJUST GEAR TROUBLE |
| 852 | 852:模具安裝位置檢査 | 852:MOLD FITTING POSITION CHECK |
| 853 | 853:油壓夾模異常檢査 | 853:HYDRAULIC CLAMP TROUBLE |
| 854 | 854:鎖模力不足檢査 | 854:CLAMP FORCE NOT ENOUGH |
| 855 | 855:機械手氣壓不足 | 855:AIR PRESSURE FOR ROBOT TOO LOW |
| 856 | 856:背壓調整過高 | 856:BACK PRESSURE TOO HIGH |
| 857 | 857:自動原料替換運行 | 857:MATERIAL CHANGE IN PROGRESS |
| 858 | 858:料管度預熱中 | 858:PREHEAT IN PROGRESS |
| 859 | 859:絞芽計數開関檢査 | 859:CHECK UNSCREW COUNTING SENSOR |
| 860 | 860:模厚自動調整中 | 860:AUTO MD THICK ADJ IN PROGRESS |
| 861 | 861:鎖模力自動調整中 | 861:AUTO MD CLA FORCE ADJ IN PROG |
| 862 | 862:換模台限位器檢査 | 862:AMC TABLE L.S. ERROR |
| 863 | 863:壓力檢測訊號異常 | 863:PRESSURE SENSOR DETECT ERROR |
| 864 | 864:熔膠轉測開関檢査 | 864:PLAST RPM SENSOR DETECT ERROR |
| 865 | 865:電箱門未関 | 865:CONTROL CABINET DOOR NOT CLOSE |
| 866 | 866:電脳内部電池更換 | 866:CHANGE BATTERY |
| 867 | 867:鎖模力自動調整完成 | 867:AUTO MD CLA FORCE COMPLETE |
| 868 | 868:模厚自動調整完成 | 868:AUTO MD THICK ADJ COMPLETE |
| 869 | 869:成品不良、檢査四段位置時間設定 | 869:INJECTION SETTING NO GOOD |
| 870 | 870:料管實際度過高 | 870:BARREL TEMPERATURE TOO HIGH |
| 871 | 871:熔膠延時中 | 871:PLASTICIZATION DELAY |
| 872 | 872:調模中 | 872:MOLD ADJUST IN PROGRESS |
| 873 | 873:轉盤中 | 873:TABLE IN ROTATION |
| 874 | 874:定位桿末退 | 874:STOPPER NOT RETURN |
| 875 | 875:自動調摸故障 | 875:AUTO MOLD ADJUST ERROR |
| 876 | 876:踏板故障 | 876:STEPPER ERROR |
| 877 | 877:請按電源制時 | 877:PUSH POWER ON SWITCH TWICE |
| 878 | 878:頂針板末退 | 878:EJECTOR PLATE NOT RETURN |
| 879 | 879:安全閥故障 | 879:SAFETY VALVE ERROR |
| 880 | 880:開鎖模故障 | 880:MOLD CLAMP OPEN ALARM |
| 881 | 881:安全門限位器故障 | 881:DOOR LIMIT SWITCH ERROR |
| 882 | 882:門機械鎖故障 | 882:DOOR LATCH ERROR |
| 883 | 883:氣壓不足 | 883:AIR PRESSURE NOT ENOUGH |
| 884 | 884:安全鎖油掣故障 | 884:SAFETY VALVE ERROR |
| 885 | 885:未熔膠 | 885:PLASTICIZATION NOT DONE |
| 886 | 886:成品未脱 | 886:PREFORM NOT DROP |
| 887 | 887:開模終止故障 | 887:MOLD OPEN END ERROR |
| 888 | 888:熔膠中 | 888:PLASTICIZATION INPROGRESS |
| 889 | 889:機械手安全限位故障 | 889:ROBOT SAFETY CHECK ERROR |
| 890 | 890:機械手末回零位 | 890:ROBOT NOT ZERO RETURN |
| 891 | 891:機械手故障 | 891:ROBOT ALARM |
| 892 | 892:伺服控制故障 | 892:SERVO CONTROL ALARM |
| 893 | 893:成品頂出故障 | 893:PRODUT EJECT OUT ERROR |
| 894 | 894:開模終止位置故障 | 894:OPEN END POSITION ERROR |
| 895 | 895:安全鎖模檢出故障 | 895:SAFETY CLOSE CHECK ERROR |
| 896 | 896:熔膠末終止 | 896:PLASTICIZATION NOT END |
| 897 | 897:模胚末脱 | 897:PREFORM NOT DROP |
| 898 | 898:清除料筒膠料 | 898:CLEAN UP BARREL |
| 899 | 899:調整功能動中 | 899:ADJUSTMENT! |

# Text boxes

8th stage injection

9th stage injection

10th stage injection

Fast chassis

Slow chassis

Location parameter

Location parameter

Chassis backward

Location parameter

7th stage injection,

6th stage injection

5th stage injection,

4th stage injection,

3rd stage injection,

2nd stage injection,

1st stage injection

10th stage holding pressure

9th stage holding pressure

8th stage holding pressure,

7th stage holding pressure,

6th stage holding pressure

5th stage holding pressure

4th stage holding pressure

3rd stage holding pressure

1st stage holding pressure

2nd stage holding pressure

10th stage injection

1st stage plast,

2nd stage plast

3rd stage plast

4th stage plast

5th stage plast,

6th stage plast

7th stage plast,

8th stage plast,

9th stage plast

10th stage plast

Screw moves backward

2nd stage mold open

3rd stage mold open

Fast mold open

Decelerated mold open

Slow mold open

2nd stage mold clamp

3rd stage mold clamp

High pressure mold clamp

Low pressure mold clamp

Fast mold clamp